## Slide 1: 60 MHz and 120 MHz Transmission Options
Date: 2010-09-12
Authors:

## Slide 2: Benefits of 120 MHz transmission
160MHz transmission is not possible due to different spectrum regulations
  In China, the available band for 802.11 devices is from 5.725GHz to 5.850GHz (125MHz band)
Achieve 500 Mbps - 1 Gbps data rate at reasonable cost
# Streams | MCS | BW | #data tones / symbol | MAC Throughput*
8 | 256-QAM 3/4 | 40 MHz | 108 | 1.01 Gbps
4 | 256-QAM 3/4 | 80 MHz | 234 | 1.09 Gbps
3 | 64-QAM 2/3 | 160 MHz | 468 | 1.09 Gbps
2 | 256-QAM 3/4 | 160 MHz | 468 | 1.09 Gbps
3 | 256-QAM 3/4 | 60MHz | 168 | 588 Mbps
4 | 64-QAM 2/3 | 60MHz | 168 | 522 Mbps
2 | 64-QAM 2/3 | 120MHz | 336 | 522 Mbps
3 | 256-QAM 3/4 | 120MHz | 336 | 1.18Gbps
* Using Short GI and assume 70 % MAC efficiency

## Slide 3: Approach: Introducing 60MHz option
60 MHz option allows better spectrum sharing
  China: 2 x 60Mhz channels available (better than 1x40Mhz + 1x80MHz)
  US: 6 x 60Mhz channels available (only 5x 80Mhz channels )
60MHz offers 50% rate increase than 40MHz
  Possible to achieve ~500Mbps with 2x2 or 3x3 MIMO
Define 120MHz transmission by concatenating two 60MHz bands
  Same method as enabling 160MHz transmission with two 80MHz bands in 11ac
  Hardware re-use of 2x2 MIMO for 60MHz and SISO for 120MHz

## Slide 4: Possible Channel Allocations

## Slide 5: On Implementation
60MHz transmission
  Single 192 point FFT—Easy to implement
  One Example of 60MHz OFDM Waveform
    168 Data tones, 8 Pilot tones,3 DC tones, 6 left null tones, 7 right null tones
    168 Data tones: most convenient to define similar frequency interleavers as for 20, 40 or 80MHz transmission in 11a/n/ac.
120MHz transmission using two 60 MHz bands
  More flexible way to meet 120MHz Transmission Regulation in China by redefining 60MHz tones;
  Allows two 60MHz transmission modules support 2x2 MIMO and 120MHz transmission with little extra hardware
  Can reuse protocol framework used for 160 MHz option
Parameters | 40MHz | 60MHz | 80MHz
NCOL | 18 | 28/24/21 | 26
NROW | 6 × NBPSCS(iss) | 6/7/8 × NBPSCS(iss) | 9 × NBPSCS(iss)

## Slide 6: Spectrum of 120MHz Transmission
Two contiguous 60MHz Bands to form 120MHz
The Spectrum Meets the Chinese Spectrum Regulations

## Slide 7: Conclusions
Bandwidth expansion is a key feature of 11ac
  80 MHz mandatory; 160 MHz optional
  Lower cost solution relative to high-order MIMO
However, the use of 160MHz may be limited due to
  160MHz not possible in some geographies (e.g. China)
  Lower likelihood of finding available bandwidth since only two possible channels are available
We propose 60 MHz and 120 MHz options
  A new 60 GHz OFDM waveform is proposed
  120 MHz option is formed by concatenating two 60 GHz bands using a common protocol framework used to produce 160 MHz.