## Slide 1: Protocol for SU and MU Sounding Feedback
Date: 2010-09-14
Authors:

## Slide 2: Introduction
Define a protocol for SU-BF and MU-MIMO explicit sounding
Major goals
  Unified SU and MU protocol
    AP implements a single mechanism that can be used in both cases
  Well defined frame formats and frame exchange
    Avoids proliferation of variants that might increase implementation complexity
  Immediate feedback report after the sounding
    Ensures efficient use of the channel information

## Slide 3: Sounding and Feedback Protocol
Sounding feedback sequence starts with AP sending an NDP Announcement (NDPA) frame followed by an NDP (after SIFS)
  NDPA identifies the first responder whose response shall follow SIFS after the NDP and may identify other STAs which will be polled subsequently
STA identified as first by the NDPA shall send Sounding Feedback frame (SND FB) SIFS time after the NDP
When allowed by rules in 8021.11n-2009 section 9.9.1.4 (Multiple frame transmission in an EDCA TXOP), the AP should poll all STAs in the same TXOP
  Section 9.9.1.4 defines the rules that allow for sending multiple frames within a TXOP with SIFS separation. It also defines the recovery procedure in case of a missing response.
Note that in the SU case, the sequence is simply NDPA-NDP-SND FB

## Slide 4: Recovery mechanism
Recovery in case of a missing response follows the rules for Multiple frame transmission in an EDCA TXOP (section 9.9.1.4 in 802.11n-2009).
  Define [NDPA-NDP-1stSND FB] as a frame exchange (‘NDPA frame exchange’)
According to the rules in 9.9.1.4 the following behavior, for instance, is possible
  In case first STA does not send SND FB SIFS time after NDP
    If NDPA frame exchange is the first frame exchange of a TXOP
      AP shall terminate the transmissions of the current TXOP and proceed to exponential backoff according to the AC used for medium access to send the NDPA
    If NDPA frame exchange is not the first frame exchange of a TXOP and TXOP started with a frame that received a valid response
      AP is allowed to access the medium PIFS after NDP and send a FB Poll frame (or any other frame)
  In case STAi does not send SND FB SIFS time after a FB Poll and TXOP started with a frame that received a valid response
      AP is allowed to access the medium PIFS after current FB poll and send a FB poll to retrieve SND feedback from same or next STA1
Example of recovery for the case where multiple STAs are sounded and one STA does not send a response to a Poll

## Slide 5: Frame Formats
Frame design aims at avoiding the proliferation of variants that might increase implementation complexity
NDPA is a new control frame carrying
  a 1 byte sequence number
  STA Info Field including a list of STA IDs; other relevant information TBD
Sounding Feedback frame is an Action No-ACK frame with:
  Category: VHT
  VHT MIMO Control field with 1-byte Sounding sequence number, other TBD subfields
  Compressed Beamforming Report field TBD
Poll frame is a control frame
  Contents TBD
SU/MU feedback request is signaled in the NDP Sounding Sequence
  Exact signaling is TBD

## Slide 6: Straw poll 1
Do you accept to add to the TGac spec framework document the sounding frame exchange protocol as defined in slides 3 and 4?

## Slide 7: Straw poll 2
Do you accept to add to the TGac spec framework document the frame formats for NDPA, Poll and Sounding Feedback frames, as defined in slides 5?