## Slide 1: “L3” LONGER Range LOWER Data Rate LOWER Energy/Power Wi-Fi for the “Internet of Things”
Date: 2010-09-13
Authors:

## Slide 2: Background
OakTree Wireless Consulting is engaged in a number of projects on behalf of clients with diverse businesses where 802.11 connectivity provides important new functionality for core product lines
This work has provided interesting insight into some common market requirements for new 802.11 applications, not optimally serviced by today’s Wi-Fi offerings
OakTree is initiating industry discussion about how to best enable this market and these applications for the rapid adoption of 802.11-based technology
Informational presentation only
  Seeking dialogue and interest for offline follow-up

## Slide 3: 10 Years of Phenomenal Wi-Fi Success
Wi-Fi is clearly one of the top 10 world-changing technologies developed and deployed in the last decade
  Wi-Fi is affordable, dependable, ubiquitous and secure which has made it universally understood, desired and a necessary part of living, working and communicating
2000 – 2005: The First Wave of Wi-Fi Adoption
  PC/IT/Peripheral devices:
    Laptops, Printers, Access Points, Routers, ….
2005 – Present: The Second Wave of Wi-Fi Adoption
  Mobile Devices, Consumer Electronics:
    Smartphones, Digital Cameras, Set-top Boxes, Gaming Consoles, Picture Frames, Music Players, Televisions, …

## Slide 4: Wi-Fi Adoption Rate Forecasts
Wireless Sensor & Control (Mu) – OnWorld 2010
Moderate Scenario

## Slide 5: Coming: 3rd Wave of Wi-Fi Adoption
The “Internet of Things” (IoT)– Everything Else
  Demand for connectivity of “things” will increase rapidly, paced by the introduction of “smarts” into all kinds of contexts, from smart grids to smart homes to smart appliances
Wi-Fi connectivity is available worldwide in most homes and businesses,
  many exciting new features, products and services are suddenly possible when non-traditional devices are capable of connecting to the internet
    Sensors, instruments, monitors, controls, appliances, …
    Solutions for many of these categories already deployed
IoT devices and companion applications may truly excel at their intended purposes with:
    Optimizations already available within existing 802.11 specification
    Possible enhancements to 802.11
    Use case certifications defined by Wi-Fi Alliance
    …..
Must clearly understand Use Cases to determine next steps to take

## Slide 6: Market Awareness of Wi-Fi benefits
“There are significant benefits to the use of Low Power Embedded Wi-Fi in wireless sensor networks. The first of these is the obvious connectivity within existing Wi-Fi networks in a given application space. In the current economic environment, Low Power Embedded Wi-Fi’s reuse of existing Wi-Fi infrastructures offers a key cost savings [..]. Additionally, the built-in Internet Protocol connectivity enables much easier network deployment and management as well as the use of more well known development and management tools.”
-- InfoTECH News, May 13, 2010

## Slide 7: “Internet of Things” Major Market Segments
Energy management
  Appliances
  Thermostats
  HVAC equipment
  Metering
Medical/Health/Fitness
  Blood glucose meters
  ECG
  MRI
  Patient monitoring systems
Building automation
  HVAC systems
  Security/access control
  Lighting
Industrial/process control
  Wireless Sensor Networks
  Machine to Machine
Transportation
  In-vehicle communication
  Location-based services

## Slide 8: “Internet of Things” Characteristics
Very low power consumption if non-mains connected
  Battery operation requiring years of life
Not necessarily high throughput
Longer range and reach
Non-human usage models (M2M)
Headless (no display)
  One time easy initial setup/provision – set and forget
Highly embedded - often no host processor
Ultra-small form factors
Mobility – pedestrian and vehicular uses
These are mostly new applications/new use cases for Wi-Fi

## Slide 9: How to Meet New Use Cases?
The trend for 802.11 specification extension has primarily been towards faster PHYs, higher throughput and QoS
  Addresses requirements of IT and consumer applications such as internet access, file sharing and streaming media
  Multiple antennas and spatial diversity employed; size/power not primary design constraints
However, these are not the primary requirements/drivers of the “Internet of Things” market
  A huge market opportunity exists for wireless sensor networks which are a natural extension of the successful penetration of Wi-Fi
  The ubiquity of Wi-Fi networks is a fact that should be readily leveraged by wireless sensor applications requiring IP connectivity
  Unique characteristics of sensor applications require optimizations to meet specific sets of use cases, individually, but also sometimes collectively:
    Long Range
    Low Power/Energy
    Low Data Rate
Focus on serving these Use Cases is necessary to assure Wi-Fi can be successfully adopted by this new market

## Slide 10: Use Case Exploration
Remote, outdoor, battery-operated, parking lot payment kiosk
STA served by neighborhood, carrier, or dedicated network
  Take advantage of whatever 802.11 connectivity may pre-exist
Infrequent, intermittent network connectivity
  Status polling and command by network control application:
    Battery life, system status/health, ticket inventory, demand-based rate schedule changes, firmware updates, etc…
  User transaction processing:
    Credit/debit card authorizations, monthly pass updates, etc…
Bursty, low-volume, low bit quantity, a-periodic communication
  Time of day, demand variations (i.e., not streaming, continuous or QoS constrained)
Reasonable battery life based on service calls frequency required for ticket replenishment or other maintenance
Longer range due to variability of outdoor environment & available networks

## Slide 11: Use Case Detail – Association Burdens
Greatly variable Down/Sleep periods, based on transaction activity, network application control/polling, time of day
  Connectivity requirements could vary from seconds to possibly days (when parking lot not used on weekend)
  STA ideally remains associated, regardless of its ability to listen and respond
Beacon listen interval is an ideal mechanism, but variations between APs pose challenge:
  APs beacon listen interval is too short. APs beacon listen interval is limited to a maximum value (sometimes, in the range of minutes). This Use Case would clearly benefit from a longer beacon listen interval
Difficult to uniformly optimize power consumption or minimize heat dissipation with existing APs as settings are vendor-specific, non-standard and often undocumented
  Maximum beacon listen interval
  STA idle time before buffered data is flushed
  STA idle time before AP disassociates a station
Consequently Sensor STAs such as this Use Case will be disassociated too frequently and consume extra energy during re-association

## Slide 12: A Different Kind of QoS
Non-streaming, non-continuous traffic; The opposite of .11e
  Bursty, infrequent connections, small data payloads
AP could report its extended beaconing support, reassociation policies and data buffering capabilities
STA/AP management coordination of this Use Case:
  Kiosk STA associates to a Wi-Fi AP
  STA announces to AP that it will/would like to go to sleep for a long beacon listen interval (1 hour for example) and goes to sleep
  AP will maintain association for the STA and will buffer data intended for the STA
  Upon wake, STA connects to the AP without complete re-association and security handshaking and AP sends buffered data to STA
  STA goes to sleep again
By advertising an extended beacon listen interval and AP operational characteristics, both STA and AP coordinate to minimize re-associations and requests for retransmission

## Slide 13: Sample Standards Activities Helping to Move in the Right Direction
Systems/Application level
TIA TR-50 – Smart Device Communications
  Develops a framework and application support platforms for a wide range of IOT applications
  Coordinated with ETSI in Europe
ETSI’s M2M project
  Develops a framework and application support platforms for a wide range of IOT applications
  Coordinated with TIA and ITU
SEP 2.0 – Smart Energy Profile
  Application layer for specific market segment that would further benefit from addressing market requirements of LONGER Range, Lower Power/Energy, LOWER Data Rates
Access Level
802.11af – TVWS and 802.11ah – S1G
  Adding available worldwide spectrum for Wi-Fi below 1Ghz
  Many Devices for specific segments/applications may eventually prioritize operation in these new bands
    Better outdoor propagation characteristics
    Improved coexistence with other co-located radios
802.11 FIA – Fast Initial Authentication Study Group
  May help with the power savings for devices that briefly and infrequently join networks
Notes: See:
http://www.tiaonline.org/standards/committees/committee.cfm?comm=tr-50
and:
http://www.etsi.org/WebSite/NewsandEvents/M2M/2010_M2M_INTRO.aspx
and:

## Slide 14: Possible Next Steps?
Define detailed application/use case scenarios for Long Range, Low Data rate and Low Energy/Power applications
Examine capabilities of existing/in-progress 802.11 specifications and WFA programs for ability to support detailed use case requirements
  Gap(s) in the standard, requiring new capabilities?
    Possibly pursue 802.11 Study Group
  Requirements can be addressed by existing 802.11?
    Can these be satisfied and implemented while coexisting with standard Wi-Fi products and Certifications?
    Possibly consider new certifications within WFA?
    …?

## Slide 15: Summary
Enormous opportunity to expand the Wi-Fi ecosystem by enabling “Internet of Things”
The market requirements for this Third Wave are unique and distinct, primarily distinguished by the need for IP connectivity and leveraging the existing Wi-Fi footprint, plus:
  Longer Range
  Lower Power/Energy
  Lower Data Rate
Organize the WLAN industry to identify the best approach to support this vast market opportunity entitlement

## Slide 16: Follow-Up Interest
Bill Carney
  bill.carney@oaktreewireless.com
Garth Hillman
  garth.hillman@oaktreewireless.com