## Slide 1: CCA for RTS/CTS Operation in Wider Channels
Date: 2010-11-08
Authors:

## Slide 2: Outline
Overview of proposed 802.11ac RTS/CTS operation [1]
Definition of busy/idle channel for CTS transmission

## Slide 3: Introduction
A protocol for RTS/CTS exchange on multiple channels was proposed in [1]. Two operation modes were defined: Static and Dynamic
If an initiator operates in dynamic operation mode:
  Upon receiving a TBD-RTS frame and if NAV at the responder is not set, a responder shall respond with a non-HT TBD-CTS over the primary channel and may respond over the secondary channels that are indicated in the TBD-RTS and that have been detected idle by the responder (all transmissions shall use a valid PHY mode, i.e. 20/40/80/80+80/160MHz)
If an initiator does not operate in dynamic operation mode:
  Upon receiving a TBD-RTS frame, a responder shall respond with a non-HT duplicate TBD-CTS frame over all channels indicated in the TBD-RTS frame only if all secondary channels indicated in the TBD-RTS frame have been detected idle by the responder (a valid PHY mode shall be used, i.e. 20/40/80/80+80/160MHz)
Meaning of “busy” and “idle” was not defined

## Slide 4: Proposed definition of busy/idle channel for CTS transmission
  NAV of secondary channels is not available, since a STA is not required to be able to decode packets on secondary channels
A mechanism is needed for a STA to assess secondary channel state and determine CTS transmission channels
Proposal
For the purpose of replying with a CTS, according to the Static or Dynamic operation modes described in [1], a secondary channel is determined to be idle if
  the PHY-CCA.indication indicates an idle state during a time interval of PIFS before the start of the RTS frame
The proposal applies to the Dynamic/Static mechanisms defined in [1] and only adds the definition of idle/busy, which are left TBD in [1].

## Slide 5: Proposed definition of busy/idle channel for CTS transmission
Example for the case of Dynamic operation [1]
  On CH4 medium is busy (based on CCA indication) for a PIFS time before the RTS
  CTS cannot be sent on CH4. Also, since CTS can be sent only on valid 20/40/80/160MHz channels, CTS is sent only on 40MHz
time
time
BA
time
time
BA
Data
RTS
RTS
RTS
RTS
CTS
CTS
Interference at responder
PIFS

## Slide 6: Proposed definition of busy/idle channel for CTS transmission
The proposed criterion defines a minimum requirement for determining the idle channels on which to send CTS
  It would not be a good idea to leave the determination up to the implementation: a weak detection might be implemented, defeating the purpose of the RTS/CTS mechanism itself
  For the Dynamic mode, it is not precluded to overlay additional restrictions based on more conservative, implementation specific, mechanisms for the detection of idle/busy state
Similar criterion is used at the RTS transmitter
  RTS is sent on a secondary channels if CCA in secondary channel was idle during a PIFS time
It can be implemented with limited complexity, by storing the CCA state before RTS reception start

## Slide 7: Pre-motion 1
  Do you support updating the TGac spec framework to include the following rules for RTS/CTS exchange in multiple channels?
If an initiator operates in dynamic mode:
  Upon receiving a TBD-RTS frame and if NAV at the responder is not set, a responder shall respond with a non-HT TBD-CTS over the primary channel and may include secondary channels that are indicated in the TBD-RTS and that have been indicated idle by the PHY-CCA.indication primitive during an interval of PIFS before the RTS frame (all transmissions shall use a valid PHY mode, i.e. 20/40/80/80+80/160MHz).
If an initiator operates in static mode:
  Upon receiving a TBD-RTS frame, a responder shall respond with a non-HT duplicate TBD-CTS frame over all channels indicated in the TBD-RTS frame only if all secondary channels indicated in the TBD-RTS frame have been indicated idle by the PHY-CCA.indication primitive during an interval of PIFS before the RTS frame (a valid PHY mode shall be used, i.e. 20/40/80/80+80/160MHz)

## Slide 8: References
        [1] IEEE 802.11-10/1289r2 “RTS/CTS Operation for Wider Channels”