## Slide 1: IEEE 802.15.4g OFDM PHY Overview
Date: 2010-11-08
Authors:

## Slide 2: Design goals for SUN
PHY for outdoor wireless communication
High density deployment with up to 3 collocated networks.
Low cost device
Low power device
Robust PHY
Data rate up to 1Mbps and higher than 40kbps
Frame size up to 1500 bytes

## Slide 3: OFDM Options
802.15.4g OFDM |  | Option 1 | Option 2 | Option 3 | Option 4 | Unit
Sampling Rate |  | 1333333.333 | 666666.667 | 333333.333 | 166666.667 | Samp/sec
FFT size |  | 128 | 64 | 32 | 16 | 
Tone Spacing |  | 10416.667 | 10416.667 | 10416.667 | 10416.667 | Hz
FFT Duration |  | 96 | 96 | 96 | 96 | microsec
Guard Interval |  | 24 | 24 | 24 | 24 | microsec
Symbol Duration |  | 120 | 120 | 120 | 120 | microsec
Symbol Rate |  | 8.333 | 8.333 | 8.333 | 8.333 | kSym/sec
Active Tones |  | 104 | 52 | 26 | 14 | 
# Pilots tones |  | 8 | 4 | 2 | 2 | 
# Data Tones |  | 96 | 48 | 24 | 12 | 
# DC null tones |  | 1 | 1 | 1 | 1 | 
Approximate Signal BW |  | 1094 | 552 | 281 | 156 | kHz
Modulation Type | MCS # | Data Rates |  |  |  | 
BPSK 1/2 rate coded and 4x repetition | 0 | 100 | 50 | 25 | 13 | kbps
BPSK 1/2 rate coded and 2x repetition | 1 | 200 | 100 | 50 | 25 | kbps
QPSK 1/2 rate coded and 2x repetition | 2 | 400 | 200 | 100 | 50 | kbps
QPSK 1/2 rate coded | 3 | 800 | 400 | 200 | 100 | kbps
QPSK 3/4 rate coded | 4 | 1200 | 600 | 300 | 150 | kbps
16-QAM 1/2 rate coded | 5 | 1600 | 800 | 400 | 200 | kbps
16-QAM 3/4 rate coded | 6 | 2400 | 1200 | 600 | 300 | kbps

## Slide 4: Similarities with 802.11
Same bit-to-symbol mapping
Same convolutional encoder (1/2 rate, constraint length K=7, generator polynomial g0=133 and g1 = 171)
Same puncturer for ¾ rate coding
Same interleaver
Option 2 has the same number of active tones (52) and same number of pilot tones (4)
Similar STF, LTF, Header, Tail and Pad structure

## Slide 5: Differences with 802.11
802.11 OFDM narrow band options are based on operating clock shrink: tone spacing reduction, guard interval increase
802.15.4g options are based on different FFT sizes: constant tone spacing and cyclic prefix
 |  | Active Tones |  |  | 
Tone Spacing | Guard Interval | 14 | 26 | 52 | 104
312.5 kHz | 0.8 us |  |  | 802.11 20MHz 54Mbps | 
156.25 kHz | 1.6 us |  |  | 802.11 10MHz 27Mbps | 
78.125 kHz | 3.2 us |  |  | 802.11 5MHz 13.5Mbps | 
39.0625 kHz | 6.4 us |  |  | 802.11 2.5MHz 6.75Mbps | 
10.41667 kHz | 24 us | 802.15.4g 200kHz 300kbps | 802.15.4g 300kHz 600kbps | 802.15.4g 600kHz 800kbps | 802.15.4g 1.2MHz 800kbps
802.11ah ?

## Slide 6: Next steps to work on…
Analyze and resolve potential issues around 802.11 MAC and TG4g PHY interface (CRC, PHY settings, etc.)
Explore some new options with data rates between 800kbps and 6.75Mbpses? Further scaling down of 802.11 and/or scaling up TG4g options with data rates above 800kbps.