## Slide 1: IEEE 802.15.4g OFDM PHY Overview
Date: 2010-11-08
Authors:

## Slide 2: 802.11 PAR
This amendment defines an Orthogonal Frequency Division Multiplexing (OFDM) Physical layer (PHY) operating in the license-exempt bands below 1 GHz, e.g., 868-868.6 MHz (Europe), 950 MHz -958 MHz (Japan), 314-316 MHz, 430-434 MHz, 470-510 MHz, and 779-787 MHz (China), 917 – 923.5 MHz (Korea) and 902-928 MHz (USA), and enhancements to the IEEE 802.11 Medium Access Control (MAC) to support this PHY, and provides mechanisms that enable coexistence with other systems in the bands including IEEE 802.15.4 and IEEE P802.15.4g.
The data rates defined in this amendment optimize the rate vs range performance of the specific channelization in a given band.
This amendment also adds support for:
- transmission range up to 1 km
- data rates > 100 kbit/s
while maintaining the 802.11 WLAN user experience for fixed, outdoor, point to multi point applications.

## Slide 3: Design goals for SUN
PHY for outdoor wireless communication
High density deployment with up to 3 collocated networks.
Low cost device
Low power device
Robust PHY
Data rate up to 1Mbps and higher than 40kbps
Frame size up to 1500 bytes

## Slide 4: OFDM Options
802.15.4g OFDM |  | Option 1 | Option 2 | Option 3 | Option 4 | Unit
Sampling Rate |  | 1333333.333 | 666666.667 | 333333.333 | 166666.667 | Samp/sec
FFT size |  | 128 | 64 | 32 | 16 | 
Tone Spacing |  | 10416.667 | 10416.667 | 10416.667 | 10416.667 | Hz
FFT Duration |  | 96 | 96 | 96 | 96 | microsec
Guard Interval |  | 24 | 24 | 24 | 24 | microsec
Symbol Duration |  | 120 | 120 | 120 | 120 | microsec
Symbol Rate |  | 8.333 | 8.333 | 8.333 | 8.333 | kSym/sec
Active Tones |  | 104 | 52 | 26 | 14 | 
# Pilots tones |  | 8 | 4 | 2 | 2 | 
# Data Tones |  | 96 | 48 | 24 | 12 | 
# DC null tones |  | 1 | 1 | 1 | 1 | 
Approximate Signal BW |  | 1094 | 552 | 281 | 156 | kHz
Modulation Type | MCS # | Data Rates |  |  |  | 
BPSK 1/2 rate coded and 4x repetition | 0 | 100 | 50 | 25 | 13 | kbps
BPSK 1/2 rate coded and 2x repetition | 1 | 200 | 100 | 50 | 25 | kbps
QPSK 1/2 rate coded and 2x repetition | 2 | 400 | 200 | 100 | 50 | kbps
QPSK 1/2 rate coded | 3 | 800 | 400 | 200 | 100 | kbps
QPSK 3/4 rate coded | 4 | 1200 | 600 | 300 | 150 | kbps
16-QAM 1/2 rate coded | 5 | 1600 | 800 | 400 | 200 | kbps
16-QAM 3/4 rate coded | 6 | 2400 | 1200 | 600 | 300 | kbps

## Slide 5: Similarities with 802.11
Same bit-to-symbol mapping
Same convolutional encoder (1/2 rate, constraint length K=7, generator polynomial g0=133 and g1 = 171)
Same puncturer for ¾ rate coding
Same interleaver
Option 2 has the same number of active tones (52) and same number of pilot tones (4)
Similar STF, LTF, Header, Tail and Pad structure

## Slide 6: Differences with 802.11
802.11 OFDM narrow band options are based on operating clock shrink: tone spacing reduction, guard interval increase
802.15.4g options are based on different FFT sizes: constant tone spacing and cyclic prefix
 |  | Active Tones |  |  | 
Tone Spacing | Guard Interval | 14 | 26 | 52 | 104
312.5 kHz | 0.8 us |  |  | 802.11 20MHz 54Mbps | 
156.25 kHz | 1.6 us |  |  | 802.11 10MHz 27Mbps | 
78.125 kHz | 3.2 us |  |  | 802.11 5MHz 13.5Mbps | 
39.0625 kHz | 6.4 us |  |  | 802.11 2.5MHz 6.75Mbps | 
10.41667 kHz | 24 us | 802.15.4g 200kHz 300kbps | 802.15.4g 300kHz 600kbps | 802.15.4g 600kHz 800kbps | 802.15.4g 1.2MHz 800kbps
802.11ah

## Slide 7: Further tasks…
Analyze and resolve potential issues around 802.11 MAC and TG4g PHY interface (CRC, PHY settings, etc.)
Potential 802.11 MAC enhancement requests.
Explore some new options with data rates between 800kbps and 6.75Mbpses? Further scaling down of 802.11 and/or scaling up TG4g options with data rates above 800kbps.
TG4g Frequency Hopping, can/should we use it? Recommended not to use it. But need to find a way to make the best use of the spectrum available.
TG4g OFDM vs. 802.11 PPDU format issues or conflicts.
  Can this cause potential degradation of Rx performance via miss-reads, etc.?
  Are there other coexistence issues?

## Slide 8: Further tasks…
802.11 PHY practices that should be considered for TG4g.
  For determining channel numbers, we would like to propose using a building up data rates from a base of 200khz vs. divide by 2 mechanisms presently proposed.
  Faster TG4g OFDM data rates and impact. Should we consider 64-QAM?
Channel model characterized including Doppler spread and consideration of MIMO.
Notes: Do we need to add anything in regards to channel management?