## Slide 1: Channel model need for 802.11ah
Date: 2010-11-08
Authors:

## Slide 2: Summary
System performance depends on channel measurement/modeling
Existing measurements and models do not include the combination of applications and environments envisioned by 802.11ah
We are evaluating measurements both for single and multi-antenna (MIMO) propagation channels

## Slide 3: Existing channel model
Existing IEEE 802.11n channel model
  based on (single-antenna) measurements at 2.4GHz (Medbo et al.)
  augmented by spatial dispersion characteristics (Erceg et al.)
Main parameters included
  pathloss
  shadowing
  delay dispersion
  angular dispersion
  Doppler effect

## Slide 4: Issues
Unclear if model is applicable to 900MHz
  Channel characteristics and interference are significantly different
Pathloss scales with frequency
Many objects are smaller than a wavelength at 900MHz (~30cm) but larger than a wavelength at 5GHz (5 cm)
  Will almost certainly see big differences in delay spread (and coherence bandwidth) and shadowing
Delay spread shows a large difference (almost factor of 5) between 5.8 GHz and 900 MHz, and even more to 400MHz
  Significant degradation for incorrect guard interval and symbol time
Deployment scenario in the 900MHz band will be different from 2.4GHz and 5GHz (i.e. placed against wall instead of portable)
  Significantly larger AP footprint will create challenging congestion issues
Existing 2.4 GHz access point to client channel model is not sufficient for the 900MHz band deployment
New measurement and model is required

## Slide 5: Channel model plan
Collaboration with University of Colorado at Boulder
Plan
  Perform measurements at 900MHz in different environments
  Extract relevant parameters (pathloss, delay spread, etc.)
  Establish generic channel model
Schedule
  Jan 2011 – present preliminary results
  Mar 2011 – present final results
Advantages
  Allow comparison platform for various proposal
  Ensure that new 802.11ah PHY performs well in real environments