## Slide 1: Channel model need for 802.11ah
Date: 2011-01-20
Authors:

## Slide 2: Issues
Unclear if model is applicable to 900MHz
  Channel characteristics and interference are significantly different
Path loss scales with frequency
Many objects are smaller than a wavelength at 900MHz (~30cm) but larger than a wavelength at 5GHz (5 cm)
  Shadowing and specular reflection effects will be very different
Delay spread shows a large difference (almost factor of 5) between 5.8 GHz and 900 MHz, and even more to 400MHz
  Will almost certainly see big differences in delay spread (and coherence bandwidth)
  Significant degradation for incorrect guard interval and symbol time
Deployment scenario in the 900MHz band will be different from 2.4GHz and 5GHz (i.e. placed against wall instead of portable)
  Significantly larger AP footprint will create challenging congestion issues
Existing 2.4 GHz access point to client channel model is not sufficient for the 900MHz band deployment
New measurement and model is required

## Slide 3: Usage models
For channel models, usage is important
  Outdoor – outdoor
    Similar to Metricom…meter to pole or pole to pole
  Indoor – outdoor
    Meter to gateway or meter to computing device or pole to device in home
  Indoor-indoor
    M2M or computing device to machine
Which ones are most important to 802.11ah?
  Longer links are most likely to have delay spreads that are poor for a downbanded 2.4GHz PHY

## Slide 4: Channel model plan
Collaboration with University of Colorado at Boulder
Literature survey?
Measurement Plan
  Perform measurements at 900MHz in different environments
  Extract relevant parameters (path loss, delay spread, etc.)
  Establish generic channel model
  Possible collaboration with IIT Bombay (Mumbai) for 400MHz
Schedule
  Mar 2011 – present preliminary results
  May 2011 – present final results
Advantages
  Allow comparison platform for various proposal
  Ensure that new 802.11ah PHY performs well in real environments
Suggest a “birds of a feather” conference call to discuss whether we can move forward