## Slide 1: Spectral Mask Absolute vs Relative
Date: 2010-11-09
Authors:

## Slide 2: Abstract
Addressing CID 10088 and CID 10089 of TGmb SB0
The newest version of the text describing the TX Mask requirements in several places is confusing and appears to be incorrect
This document discusses the perceived errors and proposes fixes to each of the TX Mask descriptions

## Slide 3: Errors
dBr values and absolute values are BOTH included in description
  dBr values are relative to the max transmitted power
  Absolute values are absolute
  As transmitted power differs from one implementation or frame transmission to another, relative specification and absolute specification may differ
Proposed solution
  Remove absolute value
  Make relative value relative to max permitted by regulation

## Slide 4: Existing Clause 17.3.9.3 Transmit Spectrum Mask
  For operation using 20 MHz channel spacing, the transmitted spectrum shall have a 0 dBr (dB relative to the maximum spectral density of the signal) bandwidth not exceeding 18 MHz, –20 dBr at 11 MHz frequency offset, –28 dBr at 20 MHz frequency offset, and the maximum of –40 dBr and –53 dBm/MHz at 30 MHz frequency offset and above. The transmitted spectral density of the transmitted signal shall fall within the spectral mask, as shown in 17-13 (Transmit spectrum mask for 20 MHz transmission). The measurements shall be made using a 100 kHz resolution bandwidth and a 30 kHz video bandwidth.17.3.9.3 Transmit spectrum mask

## Slide 5: Proposed Clause 17.3.9.3 Transmit Spectrum Mask
  For operation using 20 MHz channel spacing, the transmitted spectrum shall have a 0 dBr (dB relative to the maximum permitted spectral density of the signal) bandwidth not exceeding 18 MHz, –20 dBr at 11 MHz frequency offset, –28 dBr at 20 MHz frequency offset, and the maximum of –40 dBr and –53 dBm/MHz at 30 MHz frequency offset and above. The transmitted spectral density of the transmitted signal shall fall within the spectral mask, as shown in 17-13 (Transmit spectrum mask for 20 MHz transmission). The measurements shall be made using a 100 kHz resolution bandwidth and a 30 kHz video bandwidth.
  Also P1049 L52, strike
    and –50 dBm/MHz
  P1049 L61, strike
    and –47 dBm/MHz

## Slide 6: Proposed Clause 19.3.20.1 Transmit Spectrum Mask
  When transmitting in a 20 MHz channel, the transmitted spectrum shall have a 0 dBr (dB relative to the maximum permitted spectral density of the signal) bandwidth not exceeding 18 MHz, –20 dBr at 11 MHz frequency offset, –28 dBr at 20 MHz frequency offset, and the maximum of –45 dBr and –53 dBm/MHz at 30 MHz frequency offset and above. The transmitted spectral density of the transmitted signal shall fall within the spectral mask, as shown in Figure 19-17 (Transmit spectral mask for 20 MHz transmission). The measurements shall be made using a 100 kHz resolution bandwidth and a 30 kHz video bandwidth.
  Also, on P1182 L4, strike
    and –56 dBm/MHz