## Slide 1
Slide 1
White Space Map Information
Date: 2011-01-04
Authors:

## Slide 2: Abstract
White Space Map Information needs more fields according to FCC regulation

## Slide 3: White Space Map Information
Information for available channels may different depending on device types, Fixed/Mode II device or Mode I device

## Slide 4: White Space Map
White Space Map Element format
  Frame format in current draft
  WSM Information field is country-specific
 | Element ID | Length | WSM Type | WSM Information
Octets: | 1 | 1 | 1 | variable
 | These two fields are repeated, as determined by the Length field | 
Map ID | Channel Number | Maximum Power Level
1 | 1 | 1

## Slide 5: White Space Map
Additional fields White Space Map Information
  Device Type
    Identifies the type of devices that WSM is applied
  Channel Valid Time
    Should Channel Valid Time be per each available channels or per WSM?
      Fixed or Mode II devices need the Channel Valid Time for each channel
      Mode I devices may not need the Channel Valid Time for each channel
      Mode I devices shall listen to Contact Verification Signal every 60 seconds
      Channel Valid Time may not be present according to the Device Type

## Slide 6: White Space Map
Proposed White Space Map Information
 |  |  | These three fields are repeated, as determined by the Length field |  | 
 | Device Type | Map ID | Channel Number | Maximum Power Level | Valid Time (Optional)
Octets: | 1 | 1 | 1 | 1 | 1

## Slide 7: White Space Map
Any Comments or Suggestions?