## Slide 1: IEEE 802.11a & IEEE 802.11n changes for TGah
Date: 2010-12-20
Authors:

## Slide 2: Abstract
Leverage a widely successful standard in available bands.
Re-band OFDM and MIMO operation to TGah bands and provide for narrower channels with eight clocking.
Keep IEEE 802.11 WLAN user experience through common IEEE 802.11 MAC.

## Slide 3: Re-banding and narrower channel efforts
IEEE 802.11j-2004
  4.9 GHz – 5 GHz Operation in Japan
  Introduced “half-clocked” operation using 10 MHz channel spacing
IEEE 802.11-2007
  Introduced “quarter-clocked” operation using 5 MHz channel spacing
IEEE 802.11y-2008
  3650 – 3700 MHz Operation in USA
P802.11af D0.08
  Re-band 802.11a OFDM and 802.11n OFDM with scaling to 5 & 10 MHz channel spacing

## Slide 4: Keeping 802.11 User Experience
Solutions are available today with up/down converter added to existing silicon.
Future optimized solutions possible for better power consumption and lower cost.
  Support WLAN user experience to remain as same with IEEE 802.11e, IEEE 802.11i, IEEE 802.11k, etc.
  Use of IEEE 802.11d mandatory to avoid interference in IEEE 802.11ah bands, since the bands are not uniform around the world.

## Slide 5: Features brought by 802.11n
Features for system performance enhancement
  MIMO (Separated streams)
  A-MPDU
    MPDU aggregation of broadcast traffic
  A-MSDU
Features to increase reliability
  MIMO (Spatial Multiplexing) with Space-Time Block Coding (STBC) and Beamforming help to cope with fading.
    Higher sensitivity to the time-selective fading is expected with low-frequency, low-bandwidth
  Low-Density Parity Check Codes (LDPC)

## Slide 6: References
Draft 802.11af D0.08
11-10-536-00-00af-Clause 17 changes for sub 5 MHz channel widths
11-10-1314-00-00ah-Clause 19 changes for sub 10 MHz channel widths for HT operation