## Slide 1: Use Case Scenario for TGai
Date: 2011-01-18
Authors:
Name | Affiliations | Address | Phone | email
Hitoshi MORIOKA | ROOT INC. | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com
Marc Emmelmann | Fraunhofer Fokus | Kaiserin-Augusta-Allee 31 10589 Berlin Germany | +49-30-3463-7268 | emmelmann@ieee.org
Hiroshi MANO | ROOT INC. | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-3-5719-7630 | hmano@root-hq.com
Hiroki NAKANO | Trans New Technology | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-771-7630 | cas@trans-nt.com

## Slide 2: Abstract
This presentation shows an expected use case scenario for TGai.

## Slide 3: Use Cases for TGai
Hot-Spot Pass-Through
Train V2I Access
Simultaneous channel switch of large user groups
Coupons Distribution
Toll / Weight Station Drive By

## Slide 4: Hot-Spot Pass-Through Internet Access
Actor(s):
  Users passing near AP
Device set:
  Mobile Phone  Internet Access Point  Correspondent Server(s)
Goal:
  Ability to access various Internet services in a few seconds.
Scenario(s):
  Walking user passing by AP accesses to the Internet services, his/her e-mail/twitter/facebook/etc…
  User on vehicle/train passing by AP accesses to the Internet services, his/her e-mail/twitter/facebook/etc…
  Unmanned Air Vehicle collecting surveillance data flies through a dedicated hot-spot for data download
Notes: The actor describes the entities that interact over the 802.11ai-enabled link. Often this will be one or more people, but an actor may be a machine as well. The unique characteristics of actor as it appies to fast link establishment should be described. If more than one person, describe the relationship between the two people. Traits could include level of trust, and previous history.
The device set is the total of communicating devices in the use case. Traditional use case descriptions generally cite one device, but our fast link models require that we describe the characteristics of both or all, in the case of multiple interacting devices. Characteristics may include size, power consumption, user interface capability, and bandwidth.
The goal is a concise description of what the actor wants to accomplish, including time, user interface constraints, and device constraints.
Scenario(s) are ext description of user interaction with in a particular situation. There may be more than one scenario for each use case when the actor/devices/goal is the same, but the setting or other variable is significantly different. If necessary, list the scenarios on the Use Case slide and provide backup slides with more details on the scenarios.

## Slide 5: Train V2I Access
Actor(s):
  Mobile Router(s) on train
Device set:
  (Mobile Phone/PC  Onboard AP ) Mobile Router  Internet Access Point  Internet Services
Goal:
  Providing continuous broadband Internet access to onboard passengers.
Scenario(s):
  Passengers access to the Internet services such as e-mail/twitter/facebook anytime.
  Passengers make phone calls by VoIP.
  Passengers enjoy watching online movies.
  Train operator monitors their vehicles continuously.
  Conductor transmits seat-reservation update to the reservation center anytime.
Notes: The actor describes the entities that interact over the 802.11ai-enabled link. Often this will be one or more people, but an actor may be a machine as well. The unique characteristics of actor as it appies to fast link establishment should be described. If more than one person, describe the relationship between the two people. Traits could include level of trust, and previous history.
The device set is the total of communicating devices in the use case. Traditional use case descriptions generally cite one device, but our fast link models require that we describe the characteristics of both or all, in the case of multiple interacting devices. Characteristics may include size, power consumption, user interface capability, and bandwidth.
The goal is a concise description of what the actor wants to accomplish, including time, user interface constraints, and device constraints.
Scenario(s) are ext description of user interaction with in a particular situation. There may be more than one scenario for each use case when the actor/devices/goal is the same, but the setting or other variable is significantly different. If necessary, list the scenarios on the Use Case slide and provide backup slides with more details on the scenarios.

## Slide 6: Simultaneous channel switch of large user groups
Actor(s):
  Users already connected to an AP
Device set:
  Mobile Phone  Internet Access Point  Internet Services
Goal:
  Large number of users simultaneously and smoothly switch their channel.
Scenario(s):
  A group of users is required to switch to another frequency or AP due to
    Load balancing between APs in the area
    Detected interference or regulatory requirements force to switch to another frequency band
Notes: The actor describes the entities that interact over the 802.11ai-enabled link. Often this will be one or more people, but an actor may be a machine as well. The unique characteristics of actor as it appies to fast link establishment should be described. If more than one person, describe the relationship between the two people. Traits could include level of trust, and previous history.
The device set is the total of communicating devices in the use case. Traditional use case descriptions generally cite one device, but our fast link models require that we describe the characteristics of both or all, in the case of multiple interacting devices. Characteristics may include size, power consumption, user interface capability, and bandwidth.
The goal is a concise description of what the actor wants to accomplish, including time, user interface constraints, and device constraints.
Scenario(s) are ext description of user interaction with in a particular situation. There may be more than one scenario for each use case when the actor/devices/goal is the same, but the setting or other variable is significantly different. If necessary, list the scenarios on the Use Case slide and provide backup slides with more details on the scenarios.

## Slide 7: Use Case 4: Coupons Distribution: Overview
A user passes through in front of a shop or a digital signage.
The user can get a couple of discount coupons and may connect to the Internet.
A shop or a digital signage can identify the user.
They can give him/her adaptive advertisement and coupons.

## Slide 8: Coupon Distribution
Actor(s):
  Consumers passing by shops/digital signages
Device set:
  Mobile Phone  Access Point  Coupon Distribution Server
Goal:
  Distributing coupons to consumers walking/driving by shops/digital signages.
Scenario(s):
  Consumers passing through front of shops/digital signages get discount coupons automatically.
  Operators of shops/digital signages identify users for targeted advertising.
Notes: The actor describes the entities that interact over the 802.11ai-enabled link. Often this will be one or more people, but an actor may be a machine as well. The unique characteristics of actor as it appies to fast link establishment should be described. If more than one person, describe the relationship between the two people. Traits could include level of trust, and previous history.
The device set is the total of communicating devices in the use case. Traditional use case descriptions generally cite one device, but our fast link models require that we describe the characteristics of both or all, in the case of multiple interacting devices. Characteristics may include size, power consumption, user interface capability, and bandwidth.
The goal is a concise description of what the actor wants to accomplish, including time, user interface constraints, and device constraints.
Scenario(s) are ext description of user interaction with in a particular situation. There may be more than one scenario for each use case when the actor/devices/goal is the same, but the setting or other variable is significantly different. If necessary, list the scenarios on the Use Case slide and provide backup slides with more details on the scenarios.

## Slide 9: Questions & Comments