## Slide 1: Coverage extetion for IEEE802.11ah
Date: 2011-01-12
Authors:

## Slide 2: Abstract
In this submission, ETRI’s PHY proposal to IEEE 802.11ah is included. The permuted OFDM symbol repetition technique has been introduced to extend the coverage of IEEE 802.11ah based on IEEE 802.11a/g OFDM PHY. For narrower bandwidth, the clock downing has been also proposed.

## Slide 3: Main objectives (1)
The main application of IEEE 802.11ah is sensor network, e.g. smart metering.
  The measure information at each node should be delivered to a fusion center like an access point.
Among 3C (Capacity, Cost, Coverage), Cost and Coverage are more significant than Capacity for this application.
To extend coverage with low complexity and low power, we propose a permuted OFDM symbol repetition scheme under the framework of IEEE 802.11a/g OFDM.
For lower bandwidth, clock-downing is used.

## Slide 4: Main objectives (2)
TX range of IEEE 802.11g at 2.4GHz : 100m (typical)
Carrier shifting from 2.4GHz to sub1GHz : (2x ~2.5x) 200 ~ 250m
Rx sensitivity should be improved to achieve 1km range.
MIMO 11n for 11ah: too expensive for sensor network
Simple solution : repetition (power gain + diversity gain)

## Slide 5: Main features of ETRI proposal
From baseline of IEEE 802.11a/g OFDM PHY,
  Bandwidth reduction by downing clock speed
    20MHz (1x), 10MHz(1/2 x), 5MHz(1/4 x), 2.5MHz(1/8 x)
  Permuted OFDM symbol repetition
    2x repetition (similar with frequency spreading in 802.15.4g)
      OFDM symbol repetition with subcarrier permutation.
    4x repetition (extension of 2x repetition)

## Slide 6: Downing clock frequency
By reducing the clock frequency, we can simply obtain lower bandwidth PHY.
Change of timing parameters
 | 1x | 1/2 x | 1/4 x | 1/8 x
Bandwidth | 20 MHz | 10 MHz | 5 MHz | 2.5 MHz
Subcarrier spacing | 312.5 kHz | 156.25 kHz | 78.125 kHz | 39.0625 kHz
OFDM symbol duration | 4s | 8s | 16s | 32s
GI duration | 0.8s | 1.6s | 3.2s | 6.4s
IFFT/FFT period | 3.2s | 6.4s | 12.8s | 25.6s

## Slide 7: Repetition (1)
2x repetition
  This can obtain 3dB power gain, frequency diversity gain.
4x repetition : with the similar manner
Permuted repetition

## Slide 8: Data Rate with 1/8 BW and repetition
No repetition |  |  | 2x repetition |  |  | 4x repetition |  | 
Mapping | Code rate | RATE (bps) | Mapping | Code rate | RATE | Mapping | Code rate | RATE
BPSK | 1/2 | 750kbps | BPSK | 1/2 | 375kbps | BPSK | 1/2 | 187.5kbps
BPSK | 3/4 | 1.125Mbps | BPSK | 3/4 | 562.5kbps | BPSK | 3/4 | 281.25kbps
QPSK | 1/2 | 1.5Mbps | QPSK | 1/2 | 750kbps | QPSK | 1/2 | 375kbps
QPSK | 3/4 | 2.25Mbps | QPSK | 3/4 | 1.125Mbps | QPSK | 3/4 | 562.5kbps
16QAM | 1/2 | 3Mbps | 16QAM | 1/2 | 1.5Mbps | 16QAM | 1/2 | 750kbps
16QAM | 3/4 | 4.5Mbps | 16QAM | 3/4 | 2.25Mbps | 16QAM | 3/4 | 1.125Mbps
64QAM | 2/3 | 6Mbps | 64QAM | 2/3 | 3Mbps | 64QAM | 2/3 | 1.5Mbps
64QAM | 3/4 | 6.75Mbps | 64QAM | 3/4 | 3.375Mbps | 64QAM | 3/4 | 1.6875Mbps

## Slide 9: Requirement and Stisfaction
With clock-downing and OFDM symbol repetition, we can satisfy the following requirements
  Up to 1km coverage
  At least 100kbps
  Simple solution based on IEEE 802.11a/g OFDM PHY with single antenna

## Slide 10: Conclusion
To satisfy requirements for 802.11ah, BANDWIDTH REDUCTION and OFDM SYMBOL REPETITION schemes should be included.
In ETRI proposal, we proposed
  Downing sampling clock
  Permuted OFDM symbol repetition
based on 802.11a/g OFDM PHY.
This is a minor modification of OFDM PHY. Fast time-to-market is possible.