## Slide 1: Sounding Protocol – Segmentation and Null Feedback
Date: 2011-01-18

## Slide 2: Sounding protocol in spec framework
Spec framework defines the sounding protocol as
“[…] The NDPA identifies the first responder whose response shall follow SIFS after the NDP and may identify other STAs which will be polled subsequently. The STA identified as first by the NDPA shall send Sounding Feedback frame (SND FB) SIFS time after the NDP. When allowed by rules in 802.11n-2009 section 9.9.1.4 (Multiple frame transmission in an EDCA TXOP), the AP should poll all STAs in the same TXOP.”
NDPA is defined as a control frame:1 octet sequence number; a STA Info field including a list of STA ID; when used for MU-MIMO, TBD per user dimension reduction information; other TBD information
The sounding feedback frame is an Action No Ack frame with : Category VHT; a VHT MIMO Control field with 1 octet sounding sequence and other TBD fields; a VHT Compressed Beamforming Report field
B0-B2 | B3-B5 | B6-B7 | B8-B9 | B10 | B11 | B12-B15 | B16-B23
Nc Index | Nr Index | Channel Width | Grouping | Codebook Information | Feedback Type | Reserved | Sounding Sequence
Bits: 3 | 3 | 2 | 2 | 1 | 1 | 4 | 8

## Slide 3: Summary of proposals
Sounding protocol needs more specifications
  Define a response for the cases where feedback is not available or cannot be sent
    A Null Feedback Frame is introduced in this presentation
  Identify the cases where segmentation is required and define the segmentation protocol
    Segmentation rules are defined in this presentation

## Slide 4: Null Feedback I
There are cases where a STA does not have feedback to send back to AP
  NDPA was not received and STA does not have any feedback in its memory
  Some STAs may optionally check the validity of SIG-B in NDP; if check fails STA may not store new feedback
  STA may optionally clear the feedback in its memory after a timeout
    Timeout duration might be indicated by AP or based on channel coherence time
Currently, STA can only reply with a VHT Compressed Beamforming frame
  What should the STA put in the frame, in case it does not have a valid feedback?
    Adding old/fake feedback information only creates overhead and wrong precoding
  How should the STA behave in case feedback cannot be sent due to PPDU or TXOP limitations?

## Slide 5: Null Feedback II
One option would be for the AP not to send any response
  If NDPA or Poll are the first frame, TXOP is not established and other STAs cannot be polled
  AP does not know what happened to Poll or NDP and might keep polling the same STA
We propose to introduce a short “Null Feedback” frame
STA replies with a Null Feedback frame in case STA has no valid feedback to send
If AP receives a Null Feedback frame as a response to a NDPA or Poll, it can optimize its operations
  If NDPA or poll is first frame in TXOP, the TXOP is established: allows for recovery and for polls to other STAs
  AP avoids to poll again the same STA

## Slide 6: Null feedback frame format
We propose to define the Null feedback frame as a VHT Compressed Beamforming frame without the VHT Compressed Beamforming report field and the MU Exclusive Beamforming report field
VHT MIMO control field includes an indication that the feedback frame is a Null Feedback frame
  Signaling TBD

## Slide 7: Segmentation: Introduction
Sounding Feedback might need to be split into separate segments due to large size, for some cases.
  E.g. for 8x8 160 MHz, (7,9), Ng =1, S present, Ng’ = 2: ~27KBytes
There are various reasons why feedback might need be segmented
  MPDU and A-MPDU max length limitation
  PPDU duration limitation (see appendix)
  TXOP duration limitation (see appendix)
Segmentation was already specified in 11n
Our proposal is to limit segmentation to the cases where it cannot be avoided and keep protocol simple

## Slide 8: MPDU and A-MPDU limitation
In the worst case shown in previous slide (~27KBytes), feedback does not fit in a single VHT MPDU and might not fit in a A-MPDU
  Minimum MAX MPDU length that can be supported is 4KBytes; maximum is ~11k
  Minimum MAX A-MPDU length that can be supported is 8KBytes
Either the supported max MPDU length is long enough to fit the longest feedback from the STA, or feedback might have to be segmented in multiple MPDUs
  Preference is not to force a minimum max MPDU size based on sounding capability: segmentation is needed
  Anyway, given the worst case above, more than 1 MPDU is needed in some cases
Either the supported max A-MPDU length is long enough to fit the longest feedback from the STA, or feedback might have to be segmented in multiple A-MPDUs
  A STA which is capable of a high order MIMO, is also capable of aggregating multiple MPDUs and support at least a 27KBytes A-MPDU
  Preference is to try to avoid segmentation across multiple A-MPDUs (PPDUS) and hence mandate that feedback shall be sent within same A-MPDU

## Slide 9: MPDU and A-MPDU limitation
Maximum feedback size
  E.g. for 8x8 160 MHz, (7,9), Ng =1, S present, Ng’ = 2: ~27KBytes
Minimum MMPDU size
  There is a proposal in [1] to extend it to the same size of MPDU
  Minimum max MPDU size is 4K
  In that case 7 segments are sufficient

## Slide 10: Conclusions on Segmentation
Due to limitation on the MPDU length, segmentation is needed
  This also avoids that supported MPDU length is dictated by sounding capabilities
We propose to use the similar split criteria as defined in 11n
  9.19.3 (802.11n-2009)
  […] “If necessary, the CSI Report field, Noncompressed Beamforming Report field, or Compressed Beamforming.Report field may be split into up to TBD segments. The length of each segment shall be equal number of octets for all segments except the last, which may be smaller.”
Feedback can be split only if it does not fit in a single MMPDU
  Avoids unnecessary segmentation
We propose to force segments to be sent within the same A-MPDU
  Allows for immediate, compact feedback
  Mandates a minimum A-MPDU size capability to the STA

## Slide 11: Segmentation across PPDUs
There would be conditions that potentially require segmentation across multiple A-MPDUs (PPDUs)
  Feedback frame duration exceeding the max PPDU duration (see Appendix)
  Feedback transmission exceeding the TXOP (see Appendix)
We prefer to avoid the segmentation across PPDUs
  Simplify sounding design
How to deal with above conditions is left TBD
  One option is for the STA to reply with a Null feedback frame instead of sending the Beamforming report
This topic is not addressed in this presentation

## Slide 12: Pre-motion 1
Do you support to update the spec framework document with the following rules for the segmentation of sounding feedback?
  If it would otherwise result in an MMPDU that exceeds the maximum MPDU size, the VHT Compressed Beamforming Report field may be split into up to TBD segments. The length of each segment shall be equal number of octets for all segments except the last, which may be smaller.
  All segments shall be sent within the same A-MPDU

## Slide 13: Pre-motion 2
Do you support to update the spec framework document with the introduction of a Null Sounding Feedback response frame, defined as a Compressed Beamforming Report frame without the Compressed Beamforming Report and the MU Exclusive Beamforming Report fields; Presence/absence of the above fields is indicated in the VHT MIMO Control field, with a TBD signaling.

## Slide 14: Pre-motion 3
Do you support that a STA shall reply to a NDPA or Poll frame with a Null feedback frame in case the STA has no feedback to send?

## Slide 15: References
        [1] doc.:IEEE 802.11-11/0034r0

## Slide 16: Appendix

## Slide 17: Exceeding PPDU duration
Feedback PPDU duration can exceed max PPDU duration, in specific cases
  When Bandwidth used to transmit the feedback is narrower than the bandwidth of the included feedback report (i.e narrower than NDP BW)
  AND
  MCS is low
If feedback frame is sent with same bandwidth of included feedback report (i.e. same BW of NDP), then feedback frame always fit in a PPDU
  Compressed V (7,9), Ng = 1, S with Ng’=2
  Ntx_AP = 8; Nrx_STA = 8
  Assume TX on same BW as the feedback BW
  If feedback is sent on lower BW than the BW of the feedback, duration need be multiplied for the ratio BW_feedback/BW_transmission
BW of poll frame and report field is not mandated: potentially feedback might not fit in a PPDU
  For these cases STA might reply with a short Null Feedback frame instead
MCS of feedback frame | TX time (20MHz feedback and TX BW) (similar for higher BW)
BPSK 1/2 (1ss) | 3.8ms
16QAM 3/4 (1ss) | 0.67ms
64QAM 5/6 (1ss) | 0.4ms
BPSK 1/2 (Nrx_STA ss) | 0.54ms
16QAM 3/4 (Nrx_STA ss) | 0.14ms
64QAM 5/6 (Nrx_STA ss) | 0.11ms

## Slide 18: TXOP limitation
Feedback duration is not known at AP: in SU case, client is free to choose the number of columns of V; also, it is not defined how the MCS of the feedback is chosen
  AP may budget a NAV setting for the worst case; still, due to max TXOP limitations not all the sounded STAs might be able to transmit the feedback within the TXOP
To avoid that a feedback transmission exceeds the (residual) TXOP, a STA might sends a short frame without feedback (Null feedback) instead of the full feedback, as a response to an NDPA or Poll