## Slide 1: Introductory Submission for TGah
Date: 2011-01-16
Authors:

## Slide 2: Abstract
We present PHY/MAC enhancement areas to 802.11a/g/n to meet the 802.11ah PAR
Targeted use cases are low-data rate, low-duty cycle, long-range applications, such as metering, sensor data, etc.
  < 100 Byte packets, infrequent packet transmissions (minutes/hours), 1 km ranges, long battery life (> 1 year)

## Slide 3: General Requirements
PAR requirement:
  transmission range up to 1 km
  data rates > 100 kbit/s
  while maintaining the 802.11 WLAN user experience for fixed, outdoor, point to multi point applications.
A simple baseline design is to down-clock .11a/g/n PHY to much smaller bandwidths, similar to 15.4g

## Slide 4: Example Numerology
Scale the numerology of 802.11 20MHz mode with a constant factor
  Example: Option 2 of 802.15.4g
    Corresponds to down-clocking by 30x
Table taken from 802.11-10/1305r0
Sampling Rate |  | 666666.667 | Samp/sec
FFT size |  | 64 | 
Tone Spacing |  | 10416.667 | Hz
FFT Duration |  | 96 | microsec
Guard Interval |  | 24 | microsec
Symbol Duration |  | 120 | microsec
Symbol Rate |  | 8.333 | kSym/sec
Active Tones |  | 52 | 
# Pilots tones |  | 4 | 
# Data Tones |  | 48 | 
# DC null tones |  | 1 | 
Approximate Signal BW |  | 552 | kHz
Channel Spacing |  | 667 | 
Modulation Type | MCS # | Data Rates | kbps
BPSK 1/2 rate coded and 4x repetition | 0 | 50 | kbps
BPSK 1/2 rate coded and 2x repetition | 1 | 100 | kbps
QPSK 1/2 rate coded and 2x repetition | 2 | 200 | kbps
QPSK 1/2 rate coded | 3 | 400 | kbps
QPSK 3/4 rate coded | 4 | 600 | kbps
16-QAM 1/2 rate coded | 5 | 800 | kbps
16-QAM 3/4 rate coded | 6 | 1200 | Samp/sec

## Slide 5: PHY-MAC Enhancements
PHY mechanisms to extend range
MAC header reduction to improve overhead for small packet-sizes (< 100 bytes)
Inter-Frame spacing improvements for CSMA to reduce overheads
Relay mode to save power for battery-operated devices
Support for P2P discovery and traffic
HCCA mode for streaming applications