## Slide 1: Transmission Rules for Wider Bandwidth TXOP
Date: 2011-01-17
Authors:

## Slide 2: Outline
Motivation
Transmission rules in a TXOP
  Case 1: no non-HT duplicate frame exchange in a TXOP
  Case 2: at least one non-HT duplicate frame exchange (not including RTS/CTS) in a TXOP
Conclusions

## Slide 3: Transmission rules within a wider bandwidth TXOP are not clearly defined in the current spec
Many TXOPs are not obtained through a non-HT duplicate frame exchange
  Therefore, NAV may not be correctly set at either the transmitter or the receiver
11mb v4.01, section 9.9.1.2: “The duration of a TXOP is the duration during which the TXOP holder maintains uninterrupted control of the medium …”
The following scenario would occur if the TXOP holder does not maintain uninterrupted control of the TXOP over all channels
BA
BA
PPDU for STA1
BA
BA
PPDU for STA2
EIFS+backoff
BA
BA
PPDU for STA3
interférence

## Slide 4: In some cases, no non-HT duplicate frame exchange is used in a TXOP
If there is no non-HT duplicate frame exchange in a TXOP, once the TXOP holder transmits using a narrower bandwidth, for subsequent transmissions, it cannot transmit anything wider than such bandwidth
In this case, physical carrier sensing is utilized. Once a TXOP holder losses uninterrupted control over certain channels, it cannot re-claim the channels in the same TXOP
time
time
BA
time
time
BA
PPDU for STA1
BA
BA
PPDU for STA2
EIFS+backoff
BA
BA
PPDU for STA3

## Slide 5: In some cases, there is at least one non-HT duplicate frame exchange in a TXOP
If there is at least one non-HT duplicate frame exchange (not RTS/CTS exchange) in a TXOP, the TXOP holder transmits using the same or narrower bandwidth than the bandwidth used in the first non-HT duplicate frame exchange in the same TXOP
  The first non-HT duplicate frame exchange (not RTS/CTS) determines the max bandwidth for subsequent transmissions in the same TXOP
Once NAV is set at both the transmitter and the receiver, the TXOP holder has uninterrupted control of the bandwidth occupied by the non-HT duplicate frame exchange
time
time
BA
time
time
BA
BA
BA
PPDU for STA2
BA
BA
PPDU for STA3
BAR
BAR
BAR
BAR
BA
BA
BA
BA

## Slide 6: In conclusion, two transmission rules are defined for wider bandwidth TXOP
If there is no non-HT duplicate frame exchange in a TXOP, a TXOP holder shall not transmit frames using more bandwidth than the bandwidth occupied by the preceding frame in the same TXOP
If there is at least one non-HT duplicate frame exchange (not RTS/CTS exchange) in a TXOP, a TXOP holder shall not transmit frames using more bandwidth than the bandwidth occupied by the first non-HT duplicate frame exchange in the same TXOP

## Slide 7: Pre-motion 1
Do you support updating the TGac spec framework to include the following protocol rule?
If there is no non-HT duplicate frame exchange in a TXOP to set the NAV:
  A TXOP holder shall not transmit frames using more bandwidth than the bandwidth occupied by the preceding frame in the same TXOP

## Slide 8: Pre-motion 2
  Do you support updating the TGac spec framework to include the following protocol rule?
If there is at least one non-HT duplicate frame exchange (not a RTS/CTS exchange) in a TXOP:
  A TXOP holder shall not transmit frames using more bandwidth than the bandwidth occupied by the first non-HT duplicate frame exchange in the same TXOP