## Slide 1: Bandwidth Specific TXOP Limits
Date: 2011-01-17
Authors:

## Slide 2: Abstract
The presentation describes bandwidth specific TXOP limits
  The bandwidth specific TXOP limits improve co-existence and controllability of the 802.11ac radios
The normative text is provided in 11-11-0098r0

## Slide 3: Problem statement
The 802.11ac will increase number of cases in which the primary and the non-primary channels overlap
Currently 802.11ac has inadequate rules and means to protect a primary channel over a non-primary channel
  There are no means to prioritise primary channel over non-primary channel

## Slide 4: Problem statement
January 2011
Slide 4
A BSS is not aware of the NAV of its secondary channels
  Transmissions on secondary channels may be initiated based on CCA measurement
Currently there is only one TXOP limit per AC
  The same TXOP limit will be used for primary and secondary channels
A BSS may be blocked by extensive medium occupancy of an OBSS
  High AC (VoIP) traffic of the BSS may blocked by the OBSS transmitting best effort data
    Long medium occupancy will result in starvation and priority inversion (unfairness) between OBSSs

## Slide 5: Recap of the TXOP Limit
TXOP Limit is controlling the maximum medium occupancy
  TXOP holder may decide to use any duration up to the TXOP Limit
  TXOP Limit set to 0 allows a single PPDU transmission
During a TXOP the medium is reserved for the TXOP holder
  Long TXOPs improve the throughput of the system, but may result to higher delay
TXOP Limit is part of the EDCA Parameter Set Element
  AP assigns the values for all non-AP STAs in BSS
  EDCA is the frame work of service prioritization

## Slide 6: Bandwidth specific TXOP Limits
Separate TXOP Limits for each transmission bandwidth
t
Primary
Secondary
Tertiary and
Quaternary
Quinary (5) to
Octonary (8)
80 MHz
40 MHz
20 MHz
TXOPLimit
TXOPLimit40
TXOPLimit80
TXOPLimit160
160 MHz

## Slide 7: Signalling of bandwidth specific TXOP Limits
TXOPLimits are present in Bandwidth Specific TXOP Limits Parameter Set Element
  Separate element provides backward compatibility
Own fields to set TXOP Limit for 40, 80, 160 MHz
  Legacy TXOP Limit limits 20 MHz
For example, TXOPLimit40 is calculated: TXOPLimit * (40 MHz Factor / 255)
Octets:
Element ID
Length
(3)
40 MHz
Factor
160 MHz
Factor
80 MHz
Factor
1
1
1
1
1
Bandwidth Specific TXOP Limits Parameter Set Element

## Slide 8: Key concepts
Shorter transmission time when transmitting over larger bandwidths
  The medium occupancy of secondary channels is limited by their own TXOP limits
Allow faster release of secondary channels for other primary users
  Optimal TXOP duration reservation based on available bandwidth
  Higher probability for all primary users to capture maximum bandwidth
  Improve fairness by reducing contention intensity with short TXOP limit
  Improve QoS by reducing MAC delay and packet loss

## Slide 9: Unfairness among primary users
Single, long TXOP limit for primary and secondary channels
  Long MAC delay for other primary users (delay-sensitive VoIP traffic)
  Unused TXOP duration if higher transmission bandwidth is used
High intensity of contention upon the end of TXOP duration
  Prior TXOP holder may win contention over deferring STAs (starvation)
Channel 1
Channel 2
Channel 3
Channel 4
80 MHz transmissions with long
TXOP limit result in long MAC delay
to BSSs that have primary channel at channels2 & 3
T
TXOP
AIFS
+
BO
Medium Busy
AIFS
+
BO
80 MHz transmissions with long TXOP limit result in long MAC delay to BSSs that have primary channel at channels 2 & 3 with high priority traffic of small packet size (e.g. VoIP)
TX
OP
AIFS
+
BO
Medium Busy
AIFS
+
BO
TXOP
TXOP
AIFS
+
BO
TXOP
TX
OP
P
Unused TXOP duration
in primary channel
Unused TXOP duration
in secondary channels
Primary channel
Secondary channels

## Slide 10: Advantages
Channel usage may be more precisely coordinated in OBSS situations
Optimal TXOP duration reservation based on available bandwidth (less overheads)
Improve probability of operating with 40/80 MHz bandwidth (higher data rates)
Reduce contention intensity (better fairness)
Lower MAC delay and packet loss (better QoS)
Channel 1
Channel 2
Channel 3
Channel 4
T
X
O
P
TXOP
TXOP
T
X
O
P
AIFS
+
BO
AIFS
+
BO
AIFS
+
BO
AIFS
+
BO
80 MHz transmissions
t
t
TX
OP
TXOP
TX
OP
AIFS
+
BO
AIFS
+
BO
AIFS
+
BO
AIFS
+
BO
Mixed 40/80 MHz
transmissions
TX
OP
AIFS
+
BO
Medium Busy
Medium Busy
Medium Busy
(a)
(b)

## Slide 11: Bandwidth specific medium occupancy
One timer per bandwidth
Calculates the bandwidth specific medium occupancy
Enables flexibility of the bandwidth usage at any time of the TXOP
TXOPLimit
U-TXOP
R-TXOP
TXOPLimit40
U-TXOP
R-TXOP
TXOPLimit80
R-TXOP
TXOPLimit160
R-TXOP
Primary
Secondary
Tertiary &
Quaternary
Quinary to
Octonary
Timer
Timer
Timer
Timer
U-TXOP
Used medium occupancy
Legend
R-TXOP
Remaining medium occupancy

## Slide 12: Summary
The challenges:
  There are no means to prioritise primary channel over non-primary channel
  Long TXOP limit will result in starvation (unfairness) among STAs on both primary and secondary channels
  There is only one TXOP limit
The solution:
  Bandwidth specific TXOP limit
  Shorter TXOP limit allows faster release of secondary channels for other primary users
    Means for primary channel prioritization

## Slide 13: Pre-motion
Include the normative text as described in 11-11-0098-00-00ac-Bandwidth-Specific-TXOP-Limits.doc to the 11-09-992-18-proposed-specification-framework-for-tgac.doc document