## Slide 1: Requirements for FILS Submissions coming from PAR & 5C
Date: 2011-01-17
Authors:
Name | Affiliations | Address | Phone | email
Marc Emmelmann | Fraunhofer Fokus | Kaiserin-Augusta-Allee 31 10589 Berlin Germany | +49-30-3463-7268 | emmelmann@ieee.org
Hitoshi MORIOKA | ROOT INC. | 2-14-38 Tenjin, Chuo-ku, Fukuoka 810-0001 JAPAN | +81-92-771-7630 | hmorioka@root-hq.com

## Slide 2: Abstract
This presentation summarizes technical requirements imposed on TGai contribution by the PAR & 5C document. It also includes some discussion points on how to document compliance of contributions to these requirements.

## Slide 3: From the PAR
Title:
  …. Amandment – Fast Initial Link Set Up
Scope:
  … define modifications to … 802.11 … to enable a fast initial link set-up of 802.11 STAs
Purpose:
  … define mechanisms that provide 802.11 networks with fast initial link set-up methods which do not degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11

## Slide 4: From the 5C
Compatibility:
  No changes to MAC SAP interface
  No 802.1 architectural change
Coexistence:
  No change in channel access mechanism
  No change in physical layer
  … in such a fashion to impact coexistence
Review by group of independent security experts prior to going to sponsor ballot
  As we ask the WG to forward the draft to sponsor ballot, this will have to take place before we conduct a WG letter ballot ?
  Should we require a security review of security related submission voted into the draft. Or if not a review, some statements on the degree of security. What questions do we need to ask there?
  Should we draft some questions that need to be answered for security related proposals (e.g. what are the assumptions for the presented security scheme – pre-shared keys yes or no, etc.)

## Slide 5: From presentations yielding to FILS
We have identified (potentially overlapping) phases of link set-up
  (1) AP discovery (scanning & other means to detect / find APs)
  (2) Network discovery (11u)
  (3) Link (re-) establishment including exchange of 802.11 security-related messages
  (4) Higher layer aspects (IP address assignment etc.)
Shall we ask submissions to state which aspects are addressed?
  This would allow us to see if we have covered all aspects that need to be addressed
  Allows easy identification of submissions requiring a security review (those addressing item (3) )

## Slide 6: “Conformance w/ Requirements Table”
Have each submission yielding to or supporting text for incorporation in the TGai Draft be accompanied with the following table
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | Yes / No
Does the proposal change the MAC SAP interface? | Yes / No
Does the proposal require or introduce a change to the 802.1 architecture? | Yes / No
Does the proposal introduce a change in the channel access mechanism? | Yes / No
Does the proposal introduce a change in the PHY? | Yes / No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1,3,4 (list of applicable phases)