## Slide 1: Indoor Channel Models for 802.11ah
Date: 2011-03-13
Authors:

## Slide 2: Outline
Motivation
Indoor Modeling
  Path Loss Model
  Frequency Dependency of Statistics
Indoor MIMO Channel Model Consideration for 802.11ah
Conclusion

## Slide 3: Motivations
Discuss the relationship of dependency of path loss and small scale fading on frequency across the UHF band
Provide recommendations on the indoor channel modeling for 802.11ah

## Slide 4: Indoor Modeling: Path Loss Model
Lack of applicable measurements data around 500 MHz to 700 MHz band
The closest results available are around 800 MHz and 900 MHz band
General one slope model for typically within room prediction
Multi-wall/floor path loss model might be needed for 11ah [1]
802.11n path loss Model
  PL[dB] = PL(d0)[dB] + 10nlog10(d/d0) + X
  PL[dB] = PL(d0)+10n(d/d0)+FAF (dB) + X
  PL[dB] = FSPL(d) for d ≤ dBP
  PL[dB] = FSPL(d) + 35log10(d/ dBP) d > dBP

## Slide 5: Model Comparison
Environment | Case | n | FAF (dB) | Frequency (MHz) | Ref.
Office Building 1 | Whole Building | 3.54 |  | 914 | 1
 | Same Floor | 3.27 |  | 914 | 1
 | FAF – 1 Floor |  | 12.9 | 914 | 1
 | FAF – 2 Floor |  | 18.7 | 914 | 1
 | FAF – 3 Floor |  | 24.4 | 914 | 1
 | FAF – 4 Floor |  | 27.0 | 914 | 1
Office Building 2 | Whole Building | 4.33 |  | 914 | 1
 | Same Floor | 3.25 |  | 914 | 1
 | FAF – 1 Floor |  | 16.2 | 914 | 1
 | FAF – 2 Floor |  | 27.5 | 914 | 1
 | FAF – 3 Floor |  | 31.6 | 914 | 1
All Building Office Building 1+ Office Building 2 | 1 Floor | 4.19 |  | 914 | 1
 | 2 Floor | 5.04 |  | 914 | 1
 | 3 Floor | 5.22 |  | 914 | 1

## Slide 6: One Floor Comparison

## Slide 7: Two Floors Comparison

## Slide 8: Three Floors Comparison

## Slide 9: Other References
Environment | LOS/NLOS | n | Frequency (MHz) | Ref.
Corridor | Mixture | 1 | 1700 | 2
 | Mixture | 1-3 | 433 and 861 | 2
University Building | Mixture | 5.3 | 900 | 3
 | Mixture | 5.5 | 1800 | 3
 | Mixture | 6.0 | 2300 | 3
Office | LOS | 1.6 | 900 | 4
 | NLOS1 | 2.1 | 900 | 5
 | NLOS2 | 4.5 | 900 | 5

## Slide 10: Indoor Model: Frequency Dependency of Statistics
Fading measurement [5] at 910 MHz and 1.75 GHz in an office building and university building have shown slightly less severe fading in the 910 MHz data.
The conclusion made in [5] is that the channel statistics for both NB and WB in office building and university building are nearly the same at the 910 MHz and 1.75 GHz frequency.
The channel statistics show greater variations with the type of environment than with frequency
Similar results are observed with measurements in
  Multi-story office building [6] at 850 MHz and 1.7 GHz.
  Two dissimilar office buildings [7] at 850 MHz, 1.7 GHz and 4 GHz.
  Large commercial building [8] at 850 MHz, 1.9 GHz, 4 GHz and 5.8 GHz.

## Slide 11: Reported Results (1/3)
Over 90% of transmit locations, the rms DS was slightly greater in the 1.7 GHz band [5].
The median rms DS in that band was 28 ns, as compared to a median of 26 ns for the 900 MHz band.
4-story brick building
at Carleton University
3-story building at CRC
Over 70% of transmit locations, the rms DS was slightly greater in the 900 MHz band. The difference is very marginal [5].
The median rms DS in that band was 29 ns, as compared to a median of 30 ns for the 900 MHz band.

## Slide 12: Reported Results (2/3)
Results in [7] shown that the PDPs and the cumulative distributions of RMS delay spread in two different office buildings at 850 MHz, 1.7 GHz and 4.0 GHz frequencies are closely matched
Conclusion: Virtually no statistical difference in delay spread found in the 850 MHz, 1.7 GHz and 4.0 GHz

## Slide 13: Reported Results (3/3)
Results in [8] shown that the PDPs and the cumulative distributions of RMS delay spread in large commercial building at 850 MHz, 1.7 GHz, 4.0 GHz and 5 GHz frequencies are closely matched
Conclusion: Virtually no statistical difference in delay spread found in the 850 MHz, 1.7 GHz, 4.0 GHz and 5.8 GHz

## Slide 14: MIMO Consideration
Lack of indoor MIMO model performed at 900 MHz band
The simplest way to deal with MIMO is to adopt IEEE 802.11n indoor models except the large scale modeling.
The large scale model should behave according to slide 5 or other path loss and shadowing models agreed by the members.

## Slide 15: Conclusions
Path loss model is strongly dependent on operating frequency when the frequency separation is large across the UHF band.
No or marginal difference in channel statistics (e.g. delay spread) across the UHF band.
MIMO scenario may be addressed by using the small scale characterization of the IEEE 802.11n channel model

## Slide 16: References
S. Y. Seidel and T. S. Rappaport, “914 MHz path loss prediction models for wireless communications in multifloored buildings,” IEEE Trans. Antennas Propagat., vol. 40, no.2, pp. 207-217, Feb. 1992.
R.J.C. Bultitude, “Measurements of wideband propagation characteristics for indoor radio with predictions for digital system performance,” in Proc. Wireless ’90 Conf, Calgary, Alberta, Canada, July 1990.
A. F. Toledo and A. M. D. Turkmani, “Propagation into and within buildings at 900, 1800, and 2300 MHz,” in Proc. IEEE Vehicular Techn. Conf. VTC ‘92, Denver, Colo., May 1992, pp. 633-636
K. Pahlavan and R. Ganesh, “Statistical characterization of a partitioned indoor radio channel,” in Proc. IEEE Int. Conf Commun., ICC ’92, Chicago, Ill., June 14-17, 1992, pp. 1252-1256.
R. J. C. Bultitude, S. A. Mahmoud, and W. A. Sullivan, “A comparison of indoor radio propagation characteristics at 910 MHz and 1.75 GHz,” IEEE J. Select. Areas in Comm., vol. 7, no.1, pp. 20-30, Jan. 1989.
D. M. J. Devasirvatham, R. R. Murray, and C. Banerjee, “Time delay spread measurements at 850 MHz and 1.7 GHz inside a metropolitan office building,” Electron. Letters, vol. 25, no.3, pp. 194-196, Feb. 2, 1989.
D. M. J. Devasirvatham, M. J. Krain and D. A. Rappaport, “Radio propagation measurements at 850 MHz, 1.7 GHz and 4 GHz inside two dissimilar office buildings,” Electron. Letters, vol. 26, no.7, pp. 445-447, March 1990.
D. M. J. Devasirvatham, C. Banerjee, R. R. Murray and D. A. Rappaport, “Four frequency radiowave propagation measurements of the indoor environment in a large metropolitan commercial building,” in Proc. IEEE GLOBECOM ’91 Cont. Phoenix, Ariz., pp. 1282-1286, Dec. 1991.