## Slide 1: TGaf Comments for PHY
Authors:

## Slide 2: Abstract
This presentation describes two options for the PHY layer design for 802.11af that address the following issues pointed out by comments in LB 171
  Coexistence problems due to partially-overlapping 5MHz, 10MHz and 20MHz waveforms
  Coexistence Problems due to different down-clock factors for 5MHz and 10MHz operation
  Insufficient CP duration for outdoor applications with clock down of 4
CIDS addressed include:
  CID13, CID14, CID18, CID76, CID80, CID81, CID89, CID103, CID154, CID235, CID239, CID240, CID263, CID264, CID266, CID334, CID478, CID479, CID480, CID481, CID523, CID526, CID548, CID575, CID621, CID629, CID637, CID649, CID652, CID681, CID733, CID738, CID748, CID754, CID797, CID806, CID810, CID832, CID870, CID885, CID921, CID976, CID1003, CID1005, CID1193, CID1197, CID1198, CID1199, CID1291, CID1292, CID1295, CID1296, CID1300, CID1302

## Slide 3: Problems with Current 802.11af PHY
The current PHY and channel numbering allow for partially-overlapping 5MHz, 10MHz and 20MHz waveforms
  Partially-overlapping devices cannot decode L-SIG, HT-SIG, Duration
  Only CCA.ED works
Three down-clocking factors are possible (1,2,4)
  Symbol durations of the 5 and 10MHz mode are different
  Even if the 5MHz was aligned in frequency with the Primary channel of a 10MHz BSS, only CCA.ED works
CP duration with a down-clock factor of 4 is 3.2ms
  Not sufficient for delay spreads in out door applications
  PedB has over 600ns rms delay spread
Features in 802.11ac are missing

## Slide 4: Proposal
Provide mechanism for 11ac-like coexistence of multiple BW transmissions
  STA shall be able to decode L-SIG of any PPDUs with any BW from an OBSS
Select a single FFT tone-spacing (a single down-clock factor)
  Propose either 8 or 40/6
Provide a Guard Interval which supports outdoor usage
  More than 3.2us is needed
Base the 802.11af PHY on 802.11ac

## Slide 5: Scale Operating BW to 6MHz
Define a single down-clock factor (of 11n/11ac) equal to 6.666 (40/6)
  Align 40MHz 11n/11ac BW mode to TVWS 6MHz frequency bands.
  12MHz operation obtained by down-clock of 80MHz 11ac
  5.33 CP Duration, sufficient for outdoor applications
Allow Channel Centers on 6MHz intervals centered in TVWS channels
Multi-BW, OBSS Coexistence
  Full 11n,11ac-like coexistence between different 6 and 12MHz modes with a 3MHz Primary channel
24MHz (12MHz+12MHz) mode operation available from 80+80 mode of 802.11ac
Provide for relaxed “spectral flatness” specification, for example
  Retain +/-4 dB (-42 to -2, 2 to 42), and retain +4/-6 dB (+/-43to +/-53)
  Relax to +4/-10 dB (+/-54 to +/-58)

## Slide 6: Scale Operating BW to 5MHz
Down-clock 11ac PHY by 8
  Provides 2.5/5/10/20MHz operation corresponding to 20/40/80/160MHz
  CP Duration 6.4us: sufficient for outdoor application
For every PPDU
  PLCP is repeated over 2.5MHz bands,
Ensures that one 2.5MHz segment of 5MHz transmission lies fully within a 10MHz transmission and vice-versa
For 5MHz /10MHz coexistence
  STA shall decode the L-SIG for non-aligned 2.5MHz channel with a frequency shift of +/-500kHz
  Done by digitally shifting the receive waveform on a per-packet basis

## Slide 7: Decision on Operating BW
Selecting 6MHz operating BW
  More difficult transition band requirements for TX filtering
  FCC spectral mask requirements still dominated by stop-band requirements
  Aligned OBSS channels
Selecting 5MHz operating BW
  Ensuring OBSS coexistence more cumbersome
  Requirements on receiver, or, ugly scanning and intolerant bit requirements, or disallow any operating BW besides 5MHz