## Slide 1: Proposed Resolution to CID2114
Date: 2011-07-20
Authors:

## Slide 2: Abstract
This document proposes a resolution for CID 2114 (comment on P802.11ac/D1.0). Editing instructions are contained in 11/0898r1.
A straw poll on the proposed resolution.
A pre-motion contingent on the straw poll results.

## Slide 3: CID2114 on P802.11ac/D1.0
2114 | Bill Carney | 9.3.2.7 | 72 | 52 | TR | In order to protect against all hidden nodes, CTS must be sent by all STAs that are receivers of VHT frames. To minimize overhead, a VHT RTS frame should be defined that requests all receiving STAs to sequentially send CTSs. | As specified in 11-11-0898-00-01ac.

## Slide 4: Background
RTS/CTS is a legacy protection mechanism from 11g for the hidden node problem that carries forward into VHT implementations.
Support of RTS/CTS is up to the implementer; it is well known that it comes with some overhead.
Since RTS/CTS is available in VHT, it is reasonable to consider optional enhancements that reduce this overhead.
Multi-CTS is the proposed enhancement.

## Slide 5: Proposed Enhancement
Multi-CTS reduces the overhead by defining a frame for receiving a CTS sequence from polled stations.
  If Multi CTS is compared with having a separate RTS/CTS handshake per recipient before sending VHT frames, then the overhead can be considered to be smaller.
  If Multi CTS is compared with having a RTS/CTS handshake with only one of the recipients before sending VHT frames, then the overhead is larger. However, in this comparison, Multi CTS will be more effective for reducing collisions in scenarios where there are multiple hidden nodes which is likely to be the case in VHT deployments.
For VHT implementers choosing to optionally support RTS/CTS, Multi CTS reduces the overhead of the legacy capability in support of the overall performance expected from VHT systems.

## Slide 6: Reference Document
11-11-0898-00-01ac-resolution on multiple CTS.doc

## Slide 7: Straw Poll
Do you support the resolution of CID2114 as specified in document 11/0898r1?
Result
  Yes:
  No:
  Abstain:

## Slide 8: Pre-Motion
Instruct the editor to incorporate the changes specified in doc.: IEEE 802.11-11/0898r1 into P802.11ac/D1.0.
Motion
  Moved:
  Second:
Result
  Yes:
  No:
  Abstain: