## Slide 1: Use Cases For FILS
Date: 2011-09-19
Authors:

## Slide 2: What is 802.11ai?
802.11ai — Will define the way artificially intelligent robots overtake the world using Wi-Fi.*
Actually, that’s a lie.
*https://www.cwnp.com/cwnp_wifi_blog/802-11-alphabet-soup
No public info is yet available for 802.11ai.

## Slide 3: Use Case Process
Prototypical use cases
  Establishes a small set reference use cases
  Provides summary all use cases accepted by TGai
  Sets criteria for 802.11ai submissions
Full set of use case in
  11-11-0238-19-00ai-Use-Case-Reference-List-for-TGai.docx

## Slide 5: Definitions (1 of 2)
FILS = Fast Initial Link Setup
Device set
  mobile STA
  network access point
Use Case Differences
  Link-Attempt Rate
  Media Load
  Coverage Interval
  Link Setup Time

## Slide 6: Definitions (2 of 2)
Link-Attempt Rate
  Connection attempts per second
Media Load
  “Busyness” of the medium
Coverage Interval
  Time within the range
Link Setup Time
  Tolerable time to connect

## Slide 7: Tokyo Central Station

## Slide 8: Tokyo Central Station Use Case
Very large number of pedestrians attempt to connect at virtually the same time
General internet access with graphics and video
  Link-Attempt Rate: 100s/second
  Media Load: 50%
  Coverage Interval <10 sec
  Link Setup Time 100 ms
Driver for the adoption of FILS

## Slide 9: Drive-by Information

## Slide 10: Drive-by Use Case
Large number of vehicles
  uploading/downloading a large amount of information
  only in range for a short time.
Includes text, graphics, video
  Link-Attempt Rate <10
  Media Load 10 to 50%
  Coverage Interval <1 second
  Link Setup Time <100 ms
FILS is required to make the use case viable for 802.11

## Slide 11: Emergency Coordination

## Slide 12: Emergency Coordination Use Case
Establish a temporary infrastructure at an emergency
Includes: voice, text, graphics, video
  Link-Attempt Rate 10
  Media Load 10 - 50%
  Coverage Interval >10 sec
  Link Setup Time >2 seconds
Once FILS resides in the STA/AP, it will promote usage

## Slide 13: Handover from Mobbile to Wi-Fi

## Slide 14: Handover Use Case
Offload 3G/4G Mobile uses to WLAN
Includes: voice, text, graphics, video
  Link-Attempt Rate <10
  Media Load 10 - 50%
  Coverage Interval >10 sec
  Link Setup Time 200 milliseconds
Perhaps the “sleeper” application for FILS
Notes: In an interactive session (for instance, Skype video) does not always survive when switching from 3G to WLAN because getting WLAN interface operational takes too long. FILS will allow parallelization of other configurations, such as IP address resolution. Use case is to switch off one interface then switch on the other so as to have only one radio on at a time. Pre-association has started, but no association or IP configuration done as yet.

## Slide 15: Other Use Cases
Pedestrian
  Electronic Payment
  Traveller Information
  Pedestrian Signal System
Vehicle
  Electronic Payment
  Internet Access
  Emergency Services
  Inspections
  Resource Management
Transit
  Station arrival
  Passenger In-transit access
  Station Lobby
  Connection Protection
  Dynamic Transit Operations
Notes: Pedestrian
  Electronic Payment
  Traveller Information
  Internet Access
  Mobile Accessible Pedestrian Signal System
Vehicle
  Electronic Payment
  Traveller Information
  Internet Access
  Emergency Services
  Inspections
  Resource Management
Transit
  Station arrival
  Passenger In-transit access
  Station Lobby
  Connection Protection
  Dynamic Transit Operations

## Slide 16: References
11-10-1152-01-0fia-fast-initial-link-set-up-par.doc
11-11-0281-00-00ai-proposed-dynamic-mobility-use-cases-for-tgai.docx
11-11-0148-07-00ai-use-cases-for-tgai.docx
11-11-0122-00-00ai-3g-wlan-handover.pptx
11-11-0408-02-00ai-Use_Case_Characteristics_Discussion.pptx
11-11-0023-02-00ai-use-case-senario-for-tgai.pptx
11-11-0441-00-00ai-self-growing-use-cases-requiring-fast-initial-link-setup.docx
11-11-0746-00-00ai-discussion-on-how-many-aps-to-cover.ppt
11-11-0750-00-00ai-use-case-document-definitions.pptx
11-11-0619-00-00ai-use-case-network-mobility.pptx
11-11-0797-00-00ai-use-case-mobile-hotspot.pptx