## Slide 1: China S1G Spectrum Performance Analysis
Date: 2011-09-19
Authors:
Slide 1
Name | Affiliations | Address | Phone | email
Daning Gong | CATR | No.52 Huayuan Beilu，Beijing，100191 | 86-01-62300156 | Gongdaning@catr.cn
Zhendong Luo | CATR | No.52 Huayuan Beilu，Beijing，100191 | 86-01-62300171 | Luozhendong@catr.cn
Siyang Liu | CATR | No.52 Huayuan Beilu，Beijing，100191 | 86-01-62300174 | liusiyang@catr.cn
Bo Sun | ZTE Corporation | ZTE Building #10 Sth Tangyan Rd.,Xi'an, China | 86-29-88723501 | sun.bo1@zte.com.cn
Dezhi Zhang | ZTE Corporation | E3048,Bibo Road,Pudong,Shanghai,China | +8613816335629 | zhang.dezhi2@zte.com.cn
George Calcev | Huawei Technologies Co., Ltd. | 3601 Algonquin Road, Suite 1000 Rolling Meadows, IL 60008, USA |  | George.Calcev@huawei.com

## Slide 2: Outline
Coverage , throughput and use case of available China S1G spectrum are evaluated.
11ah spectrum and channelization for China is proposed in this contribution.
Slide 2

## Slide 3: 11ah Requirements
According to [1], the 11ah coverage and throughput requirements are :
  TGah R2 – The TGah amendment shall support mode of operation in which PHY data rate at least 100 Kbps is provided with coverage of 1km under regulatory constraints.
  TGah R3 – The TGah amendment shall provide at least a mode of operation capable of achieving a maximum aggregate Multi-Station data rate of 20Mbps as measured at the PHY data service access point (SAP) in S1G band
Slide 3

## Slide 4: Potential S1G Frequency Band and Regulations for 11ah in China
Frequency Band (MHz) | Max Tx Power (mW) | Channel BW
314-316, 430-432, 433.00-434.79 | 10 | 400 kHz
470-510 , 630-787 | 50 | 200KHz
470-566 ,614-787 | 5 | 1MHz
779-787 | 10 | No limitation
Slide 4

## Slide 5: Distance Vs. Rx for Each Band
Distance(m) | 314 MHz | 431 MHz | 510 MHz | 780 MHz
 | Rx (dBm) |  |  | 
500 | -89.9067 | -92.7662 | -87.3115 | -98.1762
600 | -92.8839 | -95.7434 | -90.2887 | -101.153
700 | -95.4011 | -98.2606 | -92.8059 | -103.671
800 | -97.5816 | -100.441 | -94.9864 | -105.851
900 | -99.5049 | -102.364 | -96.9097 | -107.774
1000 | -101.225 | -104.085 | -98.6302 | -109.495
Rx=Tx-PL=Tx-(8+37.6log10(d) +21log10(f/900MHz)), antenna height is assumed 15m above rooftop, according to [2]
1km coverage range requires at least about -110dBm receiver sensitivity.
Slide 5

## Slide 6: Throughput Analysis 1/2
We use spectrum efficiency from [3] Table 22-26—VHT MCSs for optional 20 MHz, NSS = 2
MCS | Data Rate(Mbps) 400ns GI | Spectrum Efficiency
16QAM 3/4 | 86.7 | 4.34
64QAM 5/6 | 144.4 | 7.22
256QAM 3/4 | 173.3 | 8.67
Slide 6

## Slide 7: Throughput Analysis 2/2
Channel BW | MCS | Throughput (Mbps)
200kHz | 16QAM 3/4 | 0.868
 | 64QAM 5/6 | 1.444
 | 256QAM 3/4 | 1.734
400kHz | 16QAM 3/4 | 1.736
 | 64QAM 5/6 | 2.888
 | 256QAM 3/4 | 3.468
1MHz | 16QAM 3/4 | 4.34
 | 64QAM 5/6 | 7.22
 | 256QAM 3/4 | 8.67
2MHz | 16QAM 3/4 | 8.68
 | 64QAM 5/6 | 14.44
 | 256QAM 3/4 | 17.34
4MHz | 16QAM 3/4 | 17.36
 | 64QAM 5/6 | 28.88
 | 256QAM 3/4 | 34.68
Throughput = Spectrum Efficiency * channel bandwidth
Slide 7

## Slide 8: Conclusion of Performance and Use Case
Slide 8
Frequency Band (MHz) | Max Tx Power (mW) | Channel BW | 1km Coverage Support (Y/N) | 20Mbps Support (Y/N) | Use case
314-316, 430-432, 433.00-434.79 | 10 | 400 kHz | TBD | N | Sensor
470-510 , 630-787 | 50 | 200KHz | TBD | N | Sensor
470-566 ,614-787 | 5 | 1MHz | TBD | N | Sensor, Backhaul of Sensor
779-787 | 10 | 1/2/4/8 MHz | TBD | Y, under 4MHz CH BW | Sensor, Backhaul of Sensor, Extend WiFi range
Better receiver sensitivity (see slide 5 ) is needed for 1km coverage range.

## Slide 9: Proposed 11ah Spectrum and Channelization for China
For performance and available spectrum point of view, we propose 11ah and channelization in China as the following:
  Band 1: 779-787MHz, mandatory
    1/2/4/8 MHz channel bandwidth
    same as other geography, easy to design
  Band 2: 314-316, 430-432, 433.00-434.79MHz, optional
    400kHz channel bandwidth
  Band 3: 470-510 , 630-779 MHz, optional
    200kHz channel bandwidth
    Plenty of spectrum resources
Slide 9

## Slide 10: References
[1] 11-11-0905-03-00ah-tgah-functional-requirements-and-evaluation-methodology
[2] 11-11-0968-01-00ah-channel-model-text
[3] Draft P802.11ac_D1.0
Slide 10