## Slide 1: Spec Framework Text for PHY Numerology
Date: 2011-9-21
Authors:

## Slide 2: Abstract
Based on motions in document 1294r1, the group adopted the following:
  The draft specification shall include support for 1 MHz, 2 MHz, 4 MHz, 8 MHz, and 16 MHz PHY transmissions
In this document we propose spec framework text for PHY numerology corresponding to the above transmission bandwidths in 802.11ah
Notes: doc.: IEEE 802.11-yy/xxxxr0

## Slide 3: Proposal on PHY numerology
Propose to have the same tone spacing for all BW modes
  Different BWs should be achieved through transmission on different number of subcarriers
  Helps in achieving co-existence if we have same symbol duration
Propose to have 64 tones for the 2 MHz mode
  Gives a long enough CP for outdoor deployments
  Minimizes new design work as 11ac already has designs for up-to 512 pt FFT
    Modes >= 2 MHz become 10x down-clocking (expansion) in terms of symbol times and other related parameters in 11ac
    1 MHz mode is the only mode which will need a new design

## Slide 4: Spec Framework Text on PHY Numerology
The 2 MHz PHY transmission shall be an OFDM based waveform consisting of a total of 64 tones (including tones allocated as pilot, guard and DC). Note: This implies a tone spacing of 31.25 kHz.
The tone spacing for all other bandwidth modes shall be same as the tone spacing in the 2 MHz mode.

## Slide 5: Motion
Add the following text to the .11ah Spec Framework document under the section header: ‘PHY Numerology’:
  The 2 MHz PHY transmission shall be an OFDM based waveform consisting of a total of 64 tones (including tones allocated as pilot, guard and DC). Note: This implies a tone spacing of 31.25 kHz.
  The tone spacing for all other bandwidth modes shall be same as the tone spacing in the 2 MHz mode.
Yes
No
Abstain