## Slide 1: 11ah Channelization of China
Date: 2011-09-21
Authors:
Slide 1
Name | Affiliations | Address | Phone | email
Daning Gong | CATR | No.52 Huayuan Beilu，Beijing，100191 | 86-01-62300156 | Gongdaning@catr.cn
Zhendong Luo | CATR | No.52 Huayuan Beilu，Beijing，100191 | 86-01-62300171 | Luozhendong@catr.cn
Siyang Liu | CATR | No.52 Huayuan Beilu，Beijing，100191 | 86-01-62300174 | liusiyang@catr.cn
Bo Sun | ZTE Corporation | ZTE Building #10 Sth Tangyan Rd.,Xi'an, China | 86-29-88723501 | sun.bo1@zte.com.cn
Dezhi Zhang | ZTE Corporation | E3048,Bibo Road,Pudong,Shanghai,China | +8613816335629 | zhang.dezhi2@zte.com.cn
George Calcev | Huawei Technologies Co., Ltd. | 3601 Algonquin Road, Suite 1000 Rolling Meadows, IL 60008, USA |  | George.Calcev@huawei.com

## Slide 2: Outline
This document proposes 11ah channelization of China for discussion.
Slide 2

## Slide 3: Context: Potential 11ah Band and Regulations of China
Frequency Band (MHz) | Device Category | Max Tx Power (mW) | Channel BW
314-316, 430-432, 433.00-434.79 | wireless remote control in civilian equipment | 10 | 400 kHz
470-510 , 630-787 | wireless microphone, wireless civilian measuring equipment | 50 | 200KHz
470-566 ,614-787 | general wireless remote control device(excluding toys) | 5 | 1MHz
779-787 | wireless remote control in civilian equipment (excluding toys) | 10 | No limitation
Slide 3

## Slide 4: Proposed 11ah Channelization
779 MHz
787 MHz
1 MHz
2 MHz
4 MHz
8 MHz
771 MHz
max e.r.p. 5 mW
max e.r.p. 10 mW
16 channels of 1MHz
4 channels of 2MHz
2 channels of 4MHz
1 channels of 8MHz
Slide 4

## Slide 5: Reference
Slide 5
11-11-0957-03-00ah-China-s1g-spectrum-regulations-v1
11-11-1296-01-00ah-potential-channelization-for-11ah