## Slide 1: 11ah Channelization of China
Date: 2011-09-21
Authors:
Slide 1
Name | Affiliations | Address | Phone | email
Daning Gong | CATR | No.52 Huayuan Beilu，Beijing，100191 | 86-01-62300156 | Gongdaning@catr.cn
Zhendong Luo | CATR | No.52 Huayuan Beilu，Beijing，100191 | 86-01-62300171 | Luozhendong@catr.cn
Siyang Liu | CATR | No.52 Huayuan Beilu，Beijing，100191 | 86-01-62300174 | liusiyang@catr.cn
Bo Sun | ZTE Corporation | ZTE Building #10 Sth Tangyan Rd.,Xi'an, China | 86-29-88723501 | sun.bo1@zte.com.cn
Dezhi Zhang | ZTE Corporation | E3048,Bibo Road,Pudong,Shanghai,China | +8613816335629 | zhang.dezhi2@zte.com.cn
George Calcev | Huawei Technologies Co., Ltd. | 3601 Algonquin Road, Suite 1000 Rolling Meadows, IL 60008, USA |  | George.Calcev@huawei.com

## Slide 2: Outline
This document proposes 11ah channelization of China for discussion.
Slide 2

## Slide 3: Context: Potential 11ah Band and Regulations of China [1]
Frequency Band (MHz) | Device Category | Max Tx Power (mW) | Channel BW
314-316, 430-432, 433.00-434.79 | wireless remote control in civilian equipment | 10 | 400 kHz
470-510 , 630-787 | wireless microphone, wireless civilian measuring equipment | 50 | 200KHz
470-566 ,614-787 | general wireless remote control device(excluding toys) | 5 | 1MHz
779-787 | wireless remote control in civilian equipment (excluding toys) | 10 | No limitation
Slide 3

## Slide 4: Considerations of Band and Channelization
Band 1: 779-787MHz [2]
  8MHz, 1/2/4/8MHz Channel bandwith
  high data rate applications have priority
Band 2: 755-779MHz
  24MHz, chosen from 614-787MHz, 1MHz channel bandwith
  low data rate applications have priority
  Reason to use 755-779MHz
    This band can be used for 11ah under Chinese regulation constrains
    More channels for 11ah, improve performance
    This band is consecutive with band 1, which lead to altogether 32 consecutive channels of 1MHz, easy to design
Slide 3

## Slide 5: Proposed 11ah Channelization
779 MHz
787 MHz
1 MHz
2 MHz
4 MHz
8 MHz
755 MHz
max e.r.p. 5 mW
max e.r.p. 10 mW
32 channels of 1MHz
4 channels of 2MHz
2 channels of 4MHz
1 channels of 8MHz
Slide 4
…….
24 channels of 1MHz
8 channels of 1MHz

## Slide 6: Reference
Slide 5
11-11-0957-03-00ah-China-s1g-spectrum-regulations-v1
11-11-1296-01-00ah-potential-channelization-for-11ah