## Slide 1
Tian Kaibo, ZTE Corp
Slide 1
Authors:
11ah PLCP Preamble Design
Date: 2011-11-07
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2
Tian Kaibo, ZTE Corp
Slide 2
Current Specification Framework
The draft specification shall include support for 1 MHz, 2 MHz, 4 MHz, 8 MHz, and 16 MHz PHY transmissions.
An 802.11ah STA shall support reception of 1 MHz and 2 MHz PHY transmissions.
The 2 MHz PHY transmission shall be an OFDM based waveform consisting of a total of 64 tones (including tones allocated as pilot, guard and DC).
The tone spacing for all other bandwidths PHY transmissions shall be same as the tone spacing in the 2 MHz PHY transmission.

## Slide 3
The Principles for PLCP Preamble Design
Compatibility
  There is no legacy device working on S1G spectrum, so the compatibility is easy to meet.
Efficiency
  The efficiency of 802.11 legacy PLCP preamble has been proved
  The MIMO feature need to be supported.
  Support to multiple bandwidth operations should be considered.
Consistency
  11ah should keep IEEE802.11 structure
  802.11 families have similar PLCP preamble design style

## Slide 4
Proposed Solution
The design of the PLCP preamble could be based on the 11n green format design.
The PLCP preamble could be composed of four parts, including AH-STF, AH-LTF, AH-SIG and AH-LTF1.
AH-STF
AH-LTF
AH-SIG
AH-LTF1
DATA
802.11ah PPDU format example

## Slide 5
More Details
Field | Function
AH-STF | Short Training Field, used for signal detecting, AGC, initial synchronization of frequency and time.
AH-LTF | Long Training Field for channel estimation, robust synchronization on frequency and time for following SIG field demodulation
AH-LTF1 | Long Training Field for channel estimation, robust synchronization on frequency and time for following data payload demodulation, to support multi streams operations.
AH-SIG | Signal field, used to carry information for decoding the 11ah PPDU, including MCS , Length, bandwidth indication, CRC, MIMO control information, etc. It could also be used to indicate some particular features , e.g. power saving

## Slide 6
Conclusion
The format of PLCP preamble for 11ah could use similar format as in legacy protocol
As proposed in this presentation, a 4-subfields format is suitable for 11ah PLCP preamble with fair overhead efficiency.
Further study is needed to decide the details of each subfield.

## Slide 7
Straw Poll
Do you agree that the 11ah specification shall support PLCP preamble consisting of at least four subfields as introduced in slide 4 and 5?
Y:
N:
A:

## Slide 8: References
[1] “11-11-1137-02-00ah-specification-framework-for-tgah”

## Slide 9
Thank you!