## Slide 1: On the Suitability of Repetition for 802.11ah
Date: 2012-01-17
Authors:

## Slide 2: Abstract
We present results on channel coherence times under low
mobility. Our results suggest that repetition schemes may
not be applicable under low mobility sensor applications.

## Slide 3: Motivation
Repetition is a simple scheme to provide error correction
  Repeat a message to be transmitted over the channel multiple times
  Hope that the channel will not corrupt in the same way all repeated messages
  Increase the energy per symbol repeated
Under i.i.d. Rayleigh fading repetition has time diversity gains
Repetition was suggested in e.g., [1], [2], [3], to increase the range in 802.11ah
In [3] several methods of repetition in the frequency or time domain were proposed for 802.11ah

## Slide 4: Simulation Parameters
Rayleigh fading (NLOS scenario)
Jakes Doppler Spectrum
Exponentially decaying delay profile
Carrier frequency 900 MHz
Scenarios
Scenario | RMS DS [ns] | Coherence bandwidth (50% correlation) [MHz]
Indoor Hotspot (TGn B) | 15 | 10.5
Urban Micro (TGn D) | 50 | 3.2
Urban Micro Outdoor-to-Indoor (TGn E) | 100 | 1.6

## Slide 5: Simulation Results
At 1 MHz and 2 MHz the frequency correlation is at least 0.5
Channel is not frequency selective
Repetition in frequency will not gain from frequency selectivity (gains merely from doubling energy per symbol)

## Slide 6: Simulation Results
The channel correlation up to 10ms for low mobility is high
For mobility of 3 km/h the channel coherence time is 71ms
Repeated symbols will face the same channel
  Gains only from doubling energy per symbol
Velocity [km/h] | Coherence time (50% correlation) [ms]
3 | 71
6 | 36
10 | 21
20 | 11
40 | 5.3
60 | 3.6

## Slide 7: Conclusions
Our simulations showed that under low mobility the
  Channel is not frequency selective
  Channel coherence time is much larger than the expected duration of a transmission
Repetition can only benefit from doubling energy/symbol
3dB requirement is based on very particular measurements
  Cannot guarantee that coverage problems would not happen in real life.
Repetition doubles transmission time
  Negative hit for energy consumption
Investigate further
  The needed supported path loss with expected TX powers
  Other techniques beyond repetition; e.g. Multi-hop

## Slide 8: References
[1] 11-11-0035-01-00ah-coverage-extension-for-ieee80211ah
[2] 11-11-1482-02-00ah-preamble-format-for-1-mhz
[3] 11-11-1490-01-00ah-repetition-schemes-for-tgah