## Slide 1: Singapore Sub 1GHz Frequency Bands and Channelization for IEEE 802.11ah
Date: 2012-1-17
Authors:

## Slide 2: Abstract
This presentation provides information on available frequency bands in Singapore and proposes the channelization for 802.11ah devices

## Slide 3: Short Range Devices
Intended for communications in confined areas of buildings as well as for localized on-site operations
Applications include Alarms, Identification systems, radio-detection, vehicle radar systems, wireless local area networks, remote controls, telecommand, telemetry and on-site paging systems
May be fixed, mobile or portable stations
May employ different types of modulation
May have speech application

## Slide 4: S1G Frequency Band Suitable for 11ah
Frequency Band (MHz) | Effective Radiated Power | Typical Application Types | TX Spurious Emissions | Applicable Radio Standards
216-217 | <=100 mW | Medical and Biological; Telemetry | ≥ 32 dB below carrier at 3 m or EN 300 220-1 | FCC Part 15 or EN 300 220-1
312-316 | <=100 mW | Radio Detection, Alarm system |  | 
433.05 – 434.79 | <=10 mW | Radio Telemetry, Telecommand |  | 
866 – 869 920 – 925 | 1 ≤ 500 mW | Radio Telemetry, Telecommand, RFID | ≥ 32 dB below carrier at 3 m; EN 300 220-1 or EN 302 208 | FCC Part 15 ; EN 300 220-1 or EN 302 208
1 RFID devices may transmit up to 2 W in 920 – 925 MHz upon approval

## Slide 5: Channelization in Singapore
928 MHz
1 MHz
2 MHz
4 MHz
920 MHz
925 MHz
869 MHz
866 MHz
434.79 MHz
433.05 MHz
312 MHz
316 MHz
217 MHz
216 MHz

## Slide 6: Conclusions
There are about 15 MHz identified in Singapore that can be used for IEEE 802.11ah devices
Channelization is proposed for 1 MHz, 2 MHz and 4MHz channels

## Slide 7: Motion 1
Move to accept the following frequency bands in Singapore in the Functional Requirement Document.
  866 – 869 MHz
  920 – 925 MHz
Move: Zander Lei Second: Wang Haiguang
Discussions: There were discussions to shift the frequency to the left for the 2MHz for 866-869MHz
Motion PASSES with unanimous consent.

## Slide 8: Straw Poll
Do you agree to the following Channelization in Singapore
928 MHz
920 MHz
925 MHz
869 MHz
866 MHz

## Slide 9: References
IDA TS SRD Technical Specification for Short Range Devices, May 2011