## Slide 1: Low Power Medium Access
Date: 2012-1-16
Authors:

## Slide 2: Low Power Medium Access

## Slide 3: Introduction
802.11ah use cases target low rate, long range applications
  Use cases accepted in [1] include meters, sensor applications, factory automation,…
In many cases, the devices benefiting from 11ah will be battery operated and will thus have strict power budget
  Several years of battery life requirement
  Devices should be in doze state as long as possible and only wake up for sending UL data or check DL updates, when necessary
Reduction of power consumption is a key target
We discuss an operation mode for STAs with strict energy budget

## Slide 4: Low power operation mode I
Battery operated devices should limit the power consumption by:
  Limiting the packet transmissions
  Limiting the awake/receive time
    For low transit power devices, RX power consumption may be comparable with TX power consumption
Listening for beacons/TIM frames consumes power
  Clock drift during long sleep requires an early wake up before Beacon/TIM
    Also, beacons/TIM frames may be late because of contention
    5min doze time, 20ppm  STA should wake up 12ms before the TBTT
  Reception of beacon/TIM may require several milliseconds
Beacon
Beacon
PS
Poll
ACK
Data
Awake Time
Awake Time
Beacon RX time
Doze

## Slide 5: Low power operation mode II
We envision that a STA with strict power consumption limitations may operate in the following mode
  The STA is in doze state most of the time
    It may not check the Beacon/TIM frames; it may not be in synch with TSF
  The STA wakes up at the desired time and sends a PS-Poll to AP
    Note that STA does not know if data is pending at AP, because it does not check the TIM
  AP shall respond immediately with either
    Data, or
    ACK frame including an indication of pending Buffered Units
      If no data is pending, STA can go back to sleep immediately

## Slide 6: Low power operation mode III
Example of a case where data is pending
Example of a case where data is not pending
Beacon
Beacon
PS
Poll
ACK
BU=1
Data
Awake Time
Doze
Doze
Beacon
Beacon
PS
Poll
ACK
BU=0
Awake Time
Doze
Doze

## Slide 7: More Data Field
In the ACK frame format as defined in 802.11 REVmbD12.0, the More Data bit can optionally be used to signal the presence of buffered units, in combination with APSD
We propose that AP shall use the More Data field in ACK frame to indicate the presence of buffered units, when ACK is an immediate response to a PS-Poll

## Slide 8: Conclusions
We discussed an operation mode where a STA is in Doze state most of the time and only wakes up to send UL data or PS-Poll to check for DL data
Response from AP shall be
  Immediate response with pending Data, or
  Immediate ACK indicating whether data is pending for the STA
    Pending data will follow
    If ACK indicates no data is pending, STA can go back to doze state

## Slide 9: Straw poll
Do you agree with defining the following operation mode
STA may send a PS-Poll at any time
AP shall respond immediately to a PS Poll with either
  Data for the requesting STA, or
  ACK frame with 1bit-field indicating
    1: traffic is buffered (as indicated in the TIM map), stay awake (i.e. a service period starts)
    0: no traffic is buffered, go back to sleep
    The bit used in current ACK frame format is the More Data field

## Slide 10: References
[1] 11/0905rx TGah Functional Requirements and Evaluation Methodology

## Slide 11: Appendix

## Slide 12: More Data field
8.2.4.1.8 More Data field
  The More Data field is 1 bit in length and is used to indicate to a STA in PS mode that more BUs are
  buffered for that STA at the AP. The More Data field is valid in individually addressed data or management type frames transmitted by an AP to a STA in PS mode. A value of 1 indicates that at least one additional buffered BU is present for the same STA.
  The More Data field is optionally set to 1 in individually addressed data type frames transmitted by a CFPollable STA to the PC in response to a CF-Poll to indicate that the STA has at least one additional buffered
  MSDU available for transmission in response to a subsequent CF-Poll.
  For a STA in which the More Data Ack subfield of its QoS Capability element is 1 and that has APSD
  enabled, an AP optionally sets the More Data field to 1 in ACK frames to this STA to indicate that the AP
  has a pending transmission for the STA.
  For a STA with TDLS peer PSM enabled and the More Data Ack subfield equal to 1 in the QoS Capability
  element of its transmitted TDLS Setup Request frame or TDLS Setup Response frame, a TDLS peer STA

## Slide 13: More Data field
  optionally sets the More Data field to 1 in ACK frames to this STA to indicate that it has a pending
  transmission for the STA.
  The More Data field is 1 in individually addressed frames transmitted by a mesh STA to a peer mesh STA
  that is either in light sleep mode or in deep sleep mode for the corresponding mesh peering, when additional BUs remain to be transmitted to this peer mesh STA.
  The More Data field is set to 0 in all other individually addressed frames.
  The More Data field is set to 1 in group addressed frames transmitted by the AP when additional group
  addressed bufferable units (BUs) remain to be transmitted by the AP during this beacon interval. The More
  Data field is set to 0 in group addressed frames transmitted by the AP when no more group addressed BUs
  remain to be transmitted by the AP during this beacon interval and in all group addressed frames transmitted by non-AP STAs.
  The More Data field is 1 in group addressed frames transmitted by a mesh STA when additional group
  addressed BUs remain to be transmitted. The More Data field is 0 in group addressed frames transmitted by a mesh STA when no more group addressed BUs remain to be transmitted.