## Slide 1: Short Beacon
Authors:

## Slide 2: Short Beacon

## Slide 3: Introduction
The concept of a short beacon frame was introduced in 11ah [1]
Previous straw poll indicates support for the following general short beacon content
Field | Comments
FC | Frame Control
BSSID | Need AP MAC Address
Short SSID | May be a Hash of SSID
TSF | 4 byte TSF sufficient to maintain sync
Change Sequence | Updated every time AP information changes
Information field | Carries essential Info, such as BW, Security support, etc.
Time to next full beacon | Indicates duration to next full beacon
Optional IEs | Short Beacon may also carry one or more IEs E.g. TIM IE
This presentation attempts to provide more details on the format and fields of the Short Beacon

## Slide 4: Use of the Short Beacon: Non Associated STAs
STA uses the Short Beacon to determine if the network it is looking for is available
  From compressed SSID
On observing a short beacon with the desired compressed SSID a STA may send an Association Request to the MAC address indicated in the short beacon
  Non associated STAs can quickly begin associating since short beacons can be sent more often
  Association Request will be rejected if the full SSID in the Association Request does not match the full SSID of the AP
    Solves the issue of multiple SSIDs mapping to the same compressed SSID
If a STA needs more information before associating it can do one of the following:
  Send a unicast probe request to the desired AP (based on compressed SSID)
  Use the full beacon time indication in the short beacon to receive the full beacon
    STA can go into sleep state until the full beacon receive time.

## Slide 5: Use of the Short Beacon: Associated STAs
Synchronization: Timestamp field is used to regularly correct the clock at associated STAs
To communicate changes in node configuration, the Short Beacon is used as follows:
  Signal that network information has changed using the “Change Sequence” field in the Short Beacon.
  STA can wake up to decode to full beacon at the full beacon arrival time
    Time to the full beacon is indicated in the Short Beacon
TIM: Short beacons can carry a TIM element
  AP may include the TIM element only in a subset of beacons, according to a schedule known to STAs

## Slide 6: Operation Mode - Example
AP may operate in the following mode
  Send a full beacon at every ‘full beacon’ interval
  Send a short beacon at every (non full) beacon interval
  Include a TIM element every N beacons (TIM period)
  F=Full beacon
  S= short beacon
  (T)= TIM present
Slide 6
F(T)
F(T)
S
S(T)
S
S(T)
S
S

## Slide 7: Frame Format of Short Beacon
Each field is discussed in detail in following slides

## Slide 8: Short Beacon Fields - I
Frame Control
  To indicate a Short Beacon we build on type/subtype field modifications proposed by 11ad
  Propose: B3 B2 = 11 B7 B6 B5 B4 = 0 0 0 1 (currently reserved) as indication of Short Beacon
SA: MAC Address of the AP
From Draft P802.11ad_D5.0.pdf

## Slide 9: Short Beacon Fields - II
Compressed SSID:
  Field is 4 bytes long and contains a representation of the SSID of the network that allows a device that already knows the network to discover it
    Suggestions: Standardized hash of full SSID
Timestamp
  4 byte LSBs of the Timestamp at the AP
  4 bytes is sufficient to keep up synchronization for a device that is already associated with the AP and has received the full AP Timestamp once
    With a 4 byte Timestamp rollover occurs every ~71 minutes
    With a +/- 20 ppm drift for the clock
      to drift by 30 min (~71/2) will take 1.4 years
    A sensor node can maintain time sync with its AP if it checks a Short Beacon as rarely as once a day
Change Sequence
  1 byte long
  Counter incremented if full beacon information changes
  Similar concept is used in TIM frames

## Slide 10: Short Beacon Fields - III
Info Field: Carries information for a new device trying to associate
  Suggested Fields
    Bandwidth 4 bits:
      0000 indicate 1MHz BSSS
      For all others bandwidth is 2 X value indicated by field
    1 bit to indicate if network support privacy
    Others: reserved or TBD
Duration to next beacon

## Slide 11: References
[1] 11/1137r3 Proposed Specification Framework for TGah

## Slide 12: Straw Polls
Do you agree to define a Full Beacon intervals, in units of the Beacon Interval?
  Y: N: A:
Do you agree with the FC type/subtype indication for the Short Beacon as shown in Slide 8
  Y: N: A:
Do you agree that the Short Beacon should include a compressed SSID field
  Y: N: A:
Do you agree that the Short Beacon should include a 4 byte Timestamp containing the 4 LSBs of the AP Timestamp
  Y: N: A:

## Slide 13: Straw Polls
Do you agree that the Short Beacon Should include a 1 byte Change Sequence Field that is incremented whenever critical network information changes
  Y: N: A:
Do you agree that the Short Beacon should optionally include a field indicating duration to next full beacon
  Y: N: A:

## Slide 14: References
[1] 11/1137 Proposed Specification Framework for TGah