## Slide 1
Date: 2012-01-18
Authors:
Uplink Throughput Performance of IEEE 80211ah Networks under OBSS Scenarios

## Slide 2
  Larger coverage range in IEEE 802.11ah network makes the OBSS problem more pronounced (limited channels but increased interference area)
The OBSS Problem
AP
Notes: May use same channel
doc.: IEEE 802.15-<doc#>
<month year>
        >
Page 2

## Slide 3: Abstract
Study the uplink throughput performance of IEEE 802.11ah network under OBSS Scenarios using two metrics:
(i) average throughput
(ii) coverage (10 percentile throughput)

## Slide 4: Indoor Multi-Floor Scenario
20 m
20 m
20 m
20 m
20 m
20 m
20 m
20 m
80 rooms in a building of 4 floors
20 rooms in each floor separated by a corridor
Room Dimensions: 20m * 20m * 5m
Building Dimension: 200m * 42m * 20m
1st floor
2nd floor
3rd floor
4th floor

## Slide 5: Topology with 2 APs and 4 STAs
Example Scenario
AP1
STA1
Randomly place APs and STAs in any of the 80 rooms
Each room can only have one AP but multiple STAs
A STA associates with an AP based on minimum indoor path loss computations
AP2
Coverage issues
Hidden terminal problem

## Slide 6: Topology with 5 APs and 10 STAs
Example Scenario
Example Scenario
At least one STA connects to each AP

## Slide 7: Topology with 10 APs and 20 STAs
Example Scenario
Example Scenario

## Slide 8: Topology with 20 APs and 40 STAs
Example Scenario

## Slide 9: Simulation Parameters
Channel Bandwidth | 2MHz
Building Dimension (L*B*H) | 200*40*20 m3
Room Dimensions (L*B*H) | 20*20*5 m3
Floor Attenuation Factors | 0, 12.9, 18.7, 24.4
Data Rate | 2.3 Mbps
TX Power | 23dBm
Antenna Gains | 3dBi
Max Communication Range | -88dBm
Max Interference Range | -92dBm
Packet Size | 1500Bytes
DIFS | 256µs
SIFS | 160µs
Slot Time | 48µs
[CWmin, CWmax] | [15, 1023]
Simulation Time | 160s
Notes: Mention that data rate basically means full buffer!! Add Snapshot time (results are quite unfair and this might change if the snapshot time is higher); I think packet size should be scaled as well to 150B.

## Slide 10
Average Throughput = 81.5Kbps
Uplink Throughput Performance (10 APs, 20 STAs)
No RTS-CTS
With RTS-CTS
Average Throughput = 140.37Kbps
Notes: Unfairness between cells

## Slide 11: Average UL Throughput with and without RTS-CTS
1 AP, 2 STAs
2 APs, 4 STAs
5 APs, 10 STAs
10 AP, 20 STA
With RTS-CTS
Without RTS-CTS
Throughput (kbps)
Chart: 
 | 855.3 | 717 | 408.89 | 140.37 | 135.55
 | 307.89 | 149.01 | 124.14 | 81.5 | 80.1
20 APs, 40 STAs
177% increased throughput
69% increased throughput

## Slide 12: Coverage (10 Percentile Throughput) Performance with RTS-CTS
Chart: 
 | 0 | 2 | 8 | 28 | 35
Throughput (kbps)
20 APs, 40 STAs
10 APs, 20 STAs
5 APs, 10 STAs
2 APs, 4 STAs
1 AP, 2 STAs
10% of the STAs have throughput below indicated value

## Slide 13: Discussions
RTS and CTS significantly improves performance
Unfairness in user throughput distribution in the presence of relatively large number of networks

## Slide 14: Appendix: Uplink Throughput Performance (1 AP, 2 STAs)
Average Throughput = 307.89Kbps
No RTS-CTS
With RTS-CTS
Average Throughput = 855.30Kbps
Notes: Emphasize here that we start with a coverage limited scenario

## Slide 15
Average Throughput = 149.01Kbps
Chittabrata Ghosh, Nokia
No RTS-CTS
Average Throughput = 717.00Kbps
Appendix: Uplink Throughput Performance (2 APs, 4 STAs)
With RTS-CTS

## Slide 16
Average Throughput = 124.14Kbps
Appendix: Uplink Throughput Performance (5 APs, 10 STAs)
No RTS-CTS
With RTS-CTS
Average Throughput = 408.89Kbps

## Slide 17
Average Throughput = 80.1Kbps
Appendix: Uplink Throughput Performance (20 APs, 40 STAs)
No RTS-CTS
With RTS-CTS
Average Throughput = 135.55Kbps