## Slide 1: Resolution to CID 5310
Date: 2012-03-07
Authors:

## Slide 2: CID 5310
Page 265, Line 05
Equation 117, denoting N_Sym_init is incorrect when both LDPC and STBC are enabled

## Slide 3: N_sym issue
The receiver evaluates the symbol number by L-SIG and the VHT-SIG-A as follows
The highlighted part of the above equation is incorrect. We illustrate the problem by the following example.
For BCC case,
For LDPC case,

## Slide 4: Example
Parameters settings:
  BW = 160 MHz BW
  MCS0
  1ss
  LDPC
  STBC
  Normal GI
  PSDU_Length = 150

## Slide 5: Example (contd)
In TX side
  N_dbps = 234, N_cbps = 468, m_STBC = 2, N_sym_init = 6
  LDPC processing
    N_pld = 1404, N_avbits=2808
    N_cw = 2, L_LDPC = 1944
    N_shrt = 540
    N_punc = 540→72, N_sym = 8
TXTIME = 44+8x4 = 76
LG Length = 39
194.4
648

## Slide 6: Example (contd.)
44
In RX side
  LG Length = 39, RXTIME = 76
  N’_SYM = 8
  N_SYM = 8
  N_SYM_init = 7
  PSDU_LENGTH = 202

## Slide 7: Example (contd.)
On RX side
  LDPC processing
    N_pld = 1638, N_avbits= 3276
    N_cw = 2, L_LDPC = 1944
    N_shrt = 306
    N_punc = 306 , N_sym = 7
However on TX side
  LDPC processing
    N_pld = 1404, N_avbits=2808
    N_cw = 2, L_LDPC = 1944
    N_shrt = 540.
    N_punc = 540→72, N_sym = 8

## Slide 8: Summary
In the example, we note that N_SYM and N_SYM_init differ by two on the TX side, when STBC is enabled.
Therefore, we should align the calculation on the RX side: remove two symbols as initial symbol number.

## Slide 9: Proposed Resolution
The equation 117 (shown above) is rewritten as follow: