## Slide 1
Authors:
Uplink Performance Comparison of PP-MAC and DCF
Date: 2012-03-12

## Slide 2: Abstract
Compared the performance of PP-MAC (enhanced PCF) with PCF [1]
Evaluated the performance of parallel acknowledgement [2]
In this presentation, compare the performance of PP-MAC with DCF under 802.11ah 2 MHz system

## Slide 3: Simulation Scenario
Num of AP: 1
Num of Stations:1024
Topology:
  Cell with a 1Km radius
  AP at the center of the cell
  Stations uniformly within the cell
Uplink

## Slide 4: Simulation Parameters
Channel Bandwidth | 2MHz
Number of STAs | 1024
Group size for PPMAC | 32
TX Power | 30dBm
Antenna Gains | 3dB
Max Communication Range | 1012 Meters (-88dBm)
Max Interference Range | 1293 Meters (-92dBm)
Packet Size | 250Bytes
Slot Time/SIFS/DIFS | 48µs/160µs/256µs
(CWmin, CWmax) | (15, 1023)
MCS | BPSK ½
Simulation time | 16s

## Slide 5: Throughput and Fairness with 1024 STAs
Notes: let us skip the PPMAC (no MD and FA curves). Please start the left figure at 0kbps and limit the datarate to 2kbps .

## Slide 6: Mac-to-Mac delay distribution (1024 STAs)
Notes: Please zoom in 0 to 1500ms. Currently it seems that 2s is the maximum delay which is not the case.

## Slide 7: Instantaneous Throughput with Bursty Traffic
1 kbps traffic only during 0-2sec
Throughput measured within 1sec interval

## Slide 8: Conclusion
PPMAC provides better throughput performance than DCF
PPMAC resolves fairness problem
Latency can be higher in very low activity scenarios
  Latency can be improved by combining PPMAC with DCF periods
Deterministic behavior of PP-MAC allows better prediction of energy consumption
Notes: Latency may be worse for pure PP-MAC in low activity scenarios. Adding variable length DCF period may help. More deterministic behavior enables better prediction of energy performance.

## Slide 9: References
[1] 11-11-1512-00-00ahr4-mac-consideration-for-802.11ah
[2] 11-12-0103-00-00ahr0-sequency-detection-for-parallel-ack

## Slide 10: Straw Poll
Do you agree that a PCF enhancement based on Probe and Pull MAC should be included in the framwork specification document?

## Slide 11: Enhanced PCF Polling Mechanism
CF Group Poll (Probe message)
Parallel ACK
CF Group Resource Allocation (Pull message)
SIFS
CF Group Poll
AP
STA1
P-ACK
STA2
STA3
STA4
P-ACK
CF Group Resource Allocation
SIFS
have data to send
have data to send
Data
SIFS
SIFS
ACK
Data
SIFS
ACK
SIFS