## Slide 1
Date: 2012-03-12
Authors:
Group Synchronized DCF

## Slide 2: Abstract
STAs with a group may be allowed to contend for the medium – idea of group synchronized DCF (GS-DCF)
Medium access window allowed to certain groups and prohibited to other groups
- AP decides on defining the medium access start and end times
Performance comparison of GS-DCF with DCF

## Slide 3: Group Medium Access in Beacon Frame
AP informed of Supported Rates, QoS Capability, QoS Traffic Capability, and Power Capability in Association Request frame from STAs
AP clusters STAs into groups and informs the group IDs in Association Response frame
Beacon frame defines the medium access time for each group

## Slide 4: Proposed Information Element
Propose to add an Information Element termed as Group Access Parameter Set (GAPS) element in the Beacon frame
GAPS element for group ‘n’ shall comprise of:
(i) GID: Group Identification
(ii) Group Access Start Time: Value of T_n
(iii) Group Interval End Time: End time of medium access
Beacon Interval
Time
Stamp
Capability Information
SSID
Supported Rates
FH
Parameter
Set
DS
Parameter
Set
CF
Parameter
Set
TIM
GrPS
Parameter
Set
Proposed IE
Beacon Frame

## Slide 5: Medium Access of STA Groups
Group i’s medium access Start Time is decided by the AP
Start Time based on number of associated / active STAs per group and priority setting per group
Group Interval End Time for i-th group is identical to prohibition time for (i+1)-th group
Group Access Start Time for Group 3

## Slide 6: Overlapping Medium Access Times among STA Groups
Overlapping medium access times for efficient medium contention, e.g., Groups 4 and 3 medium access
Overlapping medium access reduced idle medium time

## Slide 7: GS-DCF Medium Access
Beacon frame consists of information on all group synchronized medium access periods until next beacon
Time not assigned to groups is assigned for regular DCF
Beacon
Short Beacon
GAPS

## Slide 8: Simulation Parameters
GS-DCF Mechanism Parameters
  Number of groups: 5
  Group size: 20 STAs
  Packet accumulation interval 0-800ms
  Group active interval 800-1000ms
  Data rate per STA: 5 - 35 kbps
  No RTS/CTS
DCF Parameters
  Number of STAs: 100 STAs
  Active interval 0-1000ms
  Data rate per STA: 5 - 35 kbps
  No RTS/CTS

## Slide 9: Simulation Parameters
Channel Bandwidth | 2MHz
TX Power | 30dBm
Antenna Gains | 3dB
Communication Range | 100 Meters
Packet Size | 250Bytes
Slot Time/SIFS/DIFS | 48µs/160µs/256µs
(CWmin, CWmax) | (15, 1023)
MCS | BPSK ½
Simulation time | 16s

## Slide 10: Throughput Comparison between DCF and GS-DCF

## Slide 11: Summary
GAPS element proposed to be included in the Beacon frame
Only limited number of groups are allowed to contend during specified medium access window defined in the GAPS element
GS-DCF outperforms DCF with increasing number of STAs contending for the channel

## Slide 12: References
“Power Saving Possibilities for Networks Supporting a Large number of STAs,” doc.: IEEE 802.11-12/0028r1, January 2012, Renesas Mobile Corporation
“DCF Enhancements for Large Number of STAs,” doc.: IEEE 802.11-11/1255r0, September 2011, CATR

## Slide 13: Straw Poll
Do you agree to include the GAPS information element in the Beacon frame?