## Slide 1: MAC Header Compression
Authors:

## Slide 2: MAC Header Compression

## Slide 3: Introduction
  MAC header (30-36 octets in 11n) is a significant overhead for short MPDUs
  Inefficient for short-packet applications
    E.g., FR-EM document includes traffic specifications for sensors (256Bytes), and industrial process automation (64Bytes) [1]. Several other applications with very short transmit packets can be envisioned.
  Shorten the MAC header can save power and reduce medium occupancy
    Prolong battery lifetime
    Reduce medium occupancy
This presentation proposes a protocol to reduce MAC overhead
  The basic idea is to save constant information fields across packets at the transmitter/receiver so that they do not need be transmitted with each packet.

## Slide 4: Scenario
  Some devices may transmit short packets to a receiver for the entire lifetime
    e.g., sensors periodically report measurements to the same data collection device.
  MPDUs from the same transmitter to same receiver usually present same values for some of the header fields.
  E.g. A1, A2, A3, A4, portions of the CCMP header, and potentially portions of the payload
Transmitter could improve transmission efficiency by
  notify receiver of which fields are going to be constant across transmitted data frames, and the value of those fields
  omit those constant fields from all the transmitted frames thereafter

## Slide 5: Compression Setup
Tx sends a “Header-Compression Request” (HC-Req) management frame before the Data frames.
  indicates which MAC header fields have constant value across data MPDUs, and includes their constant value.
Rx responds with a “Header-Compression Response” (HC-Res) management frame.
      Rx can save locally the constant fields
      Rx can decline the request if it doesn’t have the capability or resource
After the successful exchange, data frames are sent omitting the constant fields as indicated in HC-req.
Upon reception of packets with a compressed header, receiver recovers the missing info. and reconstructs the full header.
HC Req
HC Resp
Data
ACK
ACK
ACK
ACK
ACK
Data
Data
Data
Data

## Slide 6: Example of a Compressed Data Frame
Compressed data frame includes
    A unique identifier/addresses
      A receiver needs to unambiguously determine whether it is the intended recipient of the frame
      Receiver uses the identifier to retrieve missing fields that were previously communicated via the HC-Req/HC-Res exchange
    Relevant header info that is not constant across frames
      E.g. sequence number, some necessary subfields of FC and QoS field etc.
    FCS, and payload

## Slide 7: Conclusions
MAC overhead can be reduced by storing constant information fields at the transmitter/receiver.
  E.g, saving of A3 and A4 (12 bytes) corresponds to 640us for each MPDU at MCS0-2rep
  Further compression can be achieved from CCMP fields and payload
Compression can be setup through a simple management exchange.

## Slide 8: Reference
[1] 11-11-0905-03-00ah-tgah-functional-requirements-and-evaluation-methodology

## Slide 9: Motion
Do you support to include in the spec framework, the concept of storing constant MAC header information at the transmitter/receiver through a management exchange, as an optional feature?