## Slide 1: Grouping For .11ah Networks
Date: 2012-03-12
Authors:

## Slide 2: Abstract
We consider the benefits in performance of grouping
compared to traditional DCF operation in 802.11ah

## Slide 3: Motivation
Use case 1c: Extended range hotspot [1]
  Typical scenarios may include:
    Extended home coverage
    Campus wide coverage
    Shopping malls
Overloading of the system cannot always be prevented with planning e.g.
    Users may all decide to check stocks at opening/closing of market
    If activation trigger for sensors (or M2M devices) is not time-dependent it may require that they contact the network at the same time e.g.,
      Different sensors in system monitoring of e.g., shopping mall will all report at the same time if you have smoke, fire, or water detectors and there is fire
        May be natural that high number of sensors are reporting
        It is desirable as fire department would know the extent of fire and smoke and if sprinklers are working

## Slide 4: Motivation
Performance parameters of relevant importance
  Overloading can cause unfairness
    Certain users may never get the chance to transmit
  Energy efficiency
    Laptop/cell phone batteries have finite capacity
Investigate grouping performance in terms of the above
  Considering the same grouping protocol as in [2]

## Slide 5: Simulations
1000 STAs associated with an AP
STAs are uniformly distributed within a 1km radius
Traffic model
  1000 packets/s
  Packets consist of 256 bytes
2 MHz channel

## Slide 6: Simulation Scenarios
1 group or 3 groups (randomly created)
Scenarios
  Three groups (1.0/0.0/0.0) no sleep simultaneous start
    Only STAs in a single group can contend
    DCF is used for the STAs that pass the “contention test”
    If they have traffic, contend simultaneously
    STAs that fail the test go to sleep
    Group schedules alternate with time (short beacons can be used)
  Three groups (1.0/0.0/0.0) sleep randomized start
    DCF with randomization
      Uniform in Beacon interval
    STAs listen Beacons, sleep, wake up to transmit and sleep
  1 group (1.0) sleep (DCF with sleep option)

## Slide 7: The 1000 STAs case: CDF of Delay
DCF (1 group)
3 groups not randomized
3 groups randomized
Large delays
  Normal since the system is overloaded
  Grouping of 3 groups with randomization outperforms DCF in terms of delay
Average ~184s
Average ~81s
Average ~50s

## Slide 8: The 1000 STAs case: Energy per STA
DCF (1 group)
3 groups not randomized
3 groups randomized
Energy consumption per STA is best under 3 groups with randomization
  Worst case energy consumption is better than best case consumption of DCF
  Grouping of 3 groups with randomization outperforms DCF
Randomization is needed in addition to grouping
  To avoid contention at the same time

## Slide 9: The 1000 STAs case: Packets per STA
DCF (1 group)
3 groups not randomized
3 groups randomized
Fairness improves with grouping and randomization
Jain Index of fairness with maximum at 1
  DCF: 0.4575
  3 groups no randomization: 0.7013
  3 groups randomization: 0.9168

## Slide 10: The 1000 STAs case: Energy per Packet
DCF (1 group)
3 groups not randomized
3 groups randomized
Worst case energy per packet is better under 3 groups with randomization

## Slide 11: Conclusions
Grouping with randomization outperforms DCF under an overloaded 802.11ah network
  Delay
  Energy efficiency
  Fairness
The exact parameters of grouping can be implementation specific

## Slide 12: References
[1] 11-11-0457-00-00ah-potential-compromise-of-802-11ah-use-case-document
[2] 11-12-0028-01-00ah-power-saving-possibilities-for-networks-supporting-a-large-number-of-stas

## Slide 13: Straw Poll
Do you support including STA grouping with randomized start of the content to improve channel access in the specification framework?
Y: N: A