## Slide 1: ACK Transmission
Date: 2012-3-13
Authors:

## Slide 2: Abstract
This presentation addresses an ACK transmission issue in IEEE 802.11ah, where asymmetric transmissions will likely to prevail

## Slide 3: Asymmetric Transmission
AP to STN (Downlink) vs STN to AP (Uplink)
STN has more constraints as opposed to AP
  Transmission power (power amplifier etc)
  Capability
    Transmission capability (1 MHz vs AP with 2 MHz and beyond)
    Functionalities (AP may serve different types STN)
Use Cases
  Use Case 3 : Extended range Wi-Fi
  Use Case 1 : Sensors and meters

## Slide 4: Problems
STN cannot reach as far as AP
  STN can receive Data
  AP cannot receive ACK sent by STN
  Given Data and ACK using the same modulation and coding rates
More likely where range is longer in 11ah
Data
ACK
SIFS
DIFS
AP
STN

## Slide 5: Simple Fix
Allow transmitting ACK with a different modulation and coding rate
  E.g. Data from AP using 16 QAM
  ACK may use QPSK or BPSK
Allow transmitting ACK with 1MHz PHY (MCS0-rep2) after receiving 2 MHz (or above) PHY packets
  All STN support both 1 MHz and 2 MHz PHY [Specification Framework]
  2 MHz is preferred whenever available (11-1535r0)
    Throughput and energy efficiency
  1 MHz is necessary, especially when
    Range is an issue
    STN with 1MHz transmission capability

## Slide 6: Conclusions
In 11ah, ACK from STN may not reach AP
  AP may transmit at higher power and better off in capability
  STN can receive Data but its ACK can not reach AP
  Given Data and ACK using the same modulation and coding or same channel bandwidth, e.g. 1 MHz, 2 MHz etc.
Propose to allow ACK using different modulation and coding, including MCS0-2rep

## Slide 7: Straw Poll 1
Do you agree to allow STN transmit ACK with lower (or more robust) modulation and coding rates than that of received frames from AP?

## Slide 8: Straw Poll 2
Do you agree to allow STN transmitting ACK with 1MHz PHY after received 2 MHz frames from AP?

## Slide 9: Straw Poll 3
Do you agree to allow STN transmitting ACK with narrower bandwidth PHY after received frames from AP?