## Slide 1: Considerations for PSMP Enhancements
Date: 2012-03-15
Authors:

## Slide 2: Abstract
This document discusses issues and benefits in considering enhancements to the PSMP scheme for 802.11ah

## Slide 3: 802.11ah use cases for PSMP
Sensor and meter STAs tend to have traffic patterns very different than the traditional traffic patterns assumed for the WLAN systems.
  For example, sensor and meter STAs could be configured to periodically upload their data to a server which will most likely to be very sporadic uplink traffic only
  Sensor and meter STAs can also be queried or configured by the server; when the server queries or configures a sensor and meter, it will expect that the queried data should arrive within a pre-defined interval
  Similarly the server/application will expect a confirmation for any configuration performed within a certain interval
There could be a large number of STAs in one BSS (e.g. 6000 STAs)

## Slide 4: Recap of PSMP
Uses a single PSMP frame to schedule multiple STAs instead of direct QoS(+) CF-Poll used in HCCA.
Reduces power consumption by providing UL and DL schedule at the start of the PSMP phase so that each STA
  only turns on its receiver during its DTT
  transmits only during its UTT without performing CCA

## Slide 5: PSMP Considerations
PSMP scheme could be a good fit for 11ah use case such as sensor and meters where STAs transmit small amount of data
However, current PSMP scheme may not fit the large number of devices scenario in 11ah very well
  A single PSMP action frame cannot schedule a large number of STAs
    Up to 32 STAs can be scheduled per PSMP frame
  The signaling overhead is high
    In each PSMP frame, STA_ID, transmission/reception order and duration have to signaled although they could be relatively static for senor and meter use case

## Slide 6: A Possible Approach
Extend PSMP operation to group-based PSMP operation by predefining groups of STAs and their schedule within each group
  The grouping approach from 11ac can be reused
Basically the PSMP-GroupID (instead of AID) may be used in the enhanced PSMP frame to address STAs belonging to the same group
With the group concept, more than 32 STAs (the limit of current PSMP) can be addressed per PSMP frame
STAs within a group could have predefined transmission/reception order

## Slide 7: Summary
The current PSMP mechanism is not optimal for 802.11ah use cases (especially sensors and meters)
Further investigate the enhancement of current power savings schemes:
  Group-based PSMP operation

## Slide 8: Questions / Comments ?
Thank You!

## Slide 9: References
802.11-2007
802.11n-2009

## Slide 10: Straw poll 1
Do you agree that the current PSMP mechanism is not optimal for 802.11ah use cases (especially sensors and meters)
  Yes
  No
  Abstain

## Slide 11: Straw poll 2
Do you think that PSMP could be enhanced for large number of devices ( sensor/meter type) by Grouping STAs
  Yes
  No
  Abstain