## Slide 1: AP Discovery Information Broadcasting
Date: 2012-05-04
Authors:
Name | Affiliations | Address | Phone | email
Young Hoon Kwon | Huawei Technologies Co., LTD. | 10180 Telesis Ct. Ste 165, San Diego, CA 92121 |  | younghoon.kwon@huawei.com
Yunsong Yang |  |  |  | 
Zhigang Rong |  |  |  | 

## Slide 2: Abstract
This document describes a technical proposal for TGai. In this proposal means are provided to speed-up AP/network discovery that reduces network congestion when lots of associations are requested in a given time.
Related sections of the SFD (12/0151r7)
  6. Fast network discovery
    6.2 Passive scanning

## Slide 3: Conformance w/ TGai PAR & 5C
Conformance Question | Response
Does the proposal degrade the security offered by Robust Security Network Association (RSNA) already defined in 802.11? | No
Does the proposal change the MAC SAP interface? | No
Does the proposal require or introduce a change to the 802.1 architecture? | No
Does the proposal introduce a change in the channel access mechanism? | No
Does the proposal introduce a change in the PHY? | No
Which of the following link set-up phases is addressed by the proposal? (1) AP Discovery (2) Network Discovery (3) Link (re-)establishment / exchange of security related messages (4) Higher layer aspects, e.g. IP address assignment | 1

## Slide 4: AP Discovery: Scanning
2 scanning schemes defined in IEEE :
  Passive scanning
    A STA waits until next beacon frame comes.
    Based on received beacon frame, a STA discovers APs and initiates association.
    Pros: No additional air channel occupancy for AP discovery.
    Cons: As beacon frame is broadcasted once in a while (normally in the order of 100msec), it takes more time to discover an AP.
  Active scanning
    A STA transmits a Probe Request message including specific SSID that the STA wants to associate.
    Corresponding APs that receives Probe Request send back Probe Response message including needed BSS information.
    Pros: Fast AP discovery available.
    Cons: additional air channel occupancy required, especially for the case wildcard SSID is included in Probe Request message. (In this case, every AP needs to send back Probe Response message.)

## Slide 5: AP Discovery: Scanning
Improvement on passive scanning schemes [1]
  Use of FILS beacon
    Define a very short beacon (FILS beacon) to advertise AP, transmit it much more frequently.
    FILS beacon only contains several necessary element for discovery.
    FILS beacon will not replace the traditional beacon frame, it will be sent much more frequently between traditional beacons.

## Slide 6: Usage Case for TGai
In case there are not much of incoming mobile users for an ESS,
  There are small number of Probe Request/Response messages.
  Because the number of incoming mobile users are small, the impact of Probe Request/Response messages will not be severe.
  Therefore, current active scanning scheme will work well.
In case there are many incoming mobile users for an ESS,
  Flooding of Probe Request/Response messages.
  Therefore, use of active scanning scheme will result in network overload.
  At the same time, because there are many incoming users in an ESS, there are also many Association Request/Response messages transmitted between AP and STAs.
  Therefore, active scanning scheme becomes problematic only when Association Request/Response messages transmission happen frequently.

## Slide 7: Proposed Recommendation
Have an option for Association Response message (or other management messages transmitted by APs) that enables carrying information that is needed for AP discovery, unless whole message frame is security encripted.
  When a STA initiates AP discovery process, it first waits and monitors the channel.
  If the STA receives one of messages that carries AP discovery information such as beacon, Probe Response, Measurement Pilot, or Association Response carrying AP discovery information during this period, the STA executes passive scanning process.
AP may transmit Association Responses message with AP discovery information when there are many Association Requests in a network.
  In case there are not much of Association Requests during given time, it just sends normal Association Response message that doesn’t carry AP discovery information.
Even if there are lots of Association Requests in a network, not all Association Response messages will carry AP discovery information.
  Rather, one Association Response message in every given time window will deliver AP discovery information.

## Slide 8: Proposed Recommendation
Proposed recommendation under FILS1) beacon
  Multiple FILS beacons are supposed to be transmitted between regular beacon period to reduce AP discovery time.
  If Association Response message is going to be transmitted close to that of FILS beacon (within the time window of T1), FILS beacon is not transmitted and AP discovery information is piggybacked on Association Response message.
  And regular beacon is transmitted always.
AP
Beacon
Beacon
FILS
Beacon
FILS
Beacon
FILS
Beacon
FILS
Beacon
FILS
Beacon
Asso.
Resp.
Asso.
Resp. w/
Dis. info
Asso.
Resp.
Asso.
Resp. w/
Dis. info
Asso.
Resp.
Asso.
Resp. w/
Dis. info
Asso.
Resp.
±T1
±T1
±T1
±T1
±T1
1) From here below, FILS beacon includes concept of any shortened version of beacon such as FILS beacon, short beacon, measurement pilot, etc.

## Slide 9: Benefits
Air time occupancy for (FILS) beacon transmission can be reduced as number of STAs joining increases.
No additional significant complexity increase for both APs and STAs
Need for transmitting Probe Response message is minimized, which can reduce the processing burden of APs.

## Slide 10: Straw Poll
Do you agree to add the sentence to section 6.2 Passive Scanning of TGai SFD, 12/0151r7?
  “AP can transmit AP discovery information in management packets, such as Association Response, which replaces adjacent FILS beacon transmission.”
Yes:
No:
Abstain:

## Slide 11: Motion
Move to add the sentence to section 6.2 Passive Scanning of TGai SFD, 12/0151r7.
  “AP can transmit AP discovery information in management packets, such as Association Response, which replaces adjacent FILS beacon transmission.”
Yes:
No:
Abstain:

## Slide 12: References
[1] IEEE802.11-12/0042r4, AP discovery with FILS beacon