## Slide 1: General 802.11 Links
Date: 2012-05-08
Authors:

## Slide 2: Abstract
This presentation discusses the use 802.11 associations as general 802 links and recommends the formation of a Study Group in this area.

## Slide 3: The Idea
As 802.11 becomes faster and more capable, with higher speeds, QoS, and robust security, it becomes more reasonable to use an 802.11 association as a general 802 link.
Use of 802.11 as an 802 link is already supported by 802.11 mesh. But there is no standard way to do this in the non-mesh cases.
The ability to optionally use an 802.11 association as an general 802 link should be extended to ESS (and IBSS) associations.

## Slide 4: Some Use Cases
802.1 AVB has informally requested this 802.11 extension based on a number of use cases:
  Car wiring harnesses are moving to Ethernet. If a car and the service bay of the car dealer both have 802.11, the service bay wants to be able to see the Ethernet stations on your car and automatically access diagnostic information.
  Process control and manufacturing can involve communications with moving transport containers or objections on assembly lines where there are multiple network devices within the moving item.
  Home entertainment systems would like to use a general mix of wired and wireless communications.
        Note: Some automotive and process control protocols are not IP based.
Use of 802.11 in Data Centers involves communication with multiple servers behind a station.

## Slide 5: Three Methods
Here are three methods:
  Just tell people to use 802.11 mesh since this can already be done with an MBSS (Mesh BSS).
    But some people don’t like mesh.
  Extend 802.11 by optionally adding portals so that an ESS (and IBSS) associations can be used as an 802 link.
    Why not extend 802.11 so all STAs can be bridges? See IEEE Std 802.11-2012, Clause P.4, “Integration service versus bridging”.
  Hide all the network that might be behind a non-AP, non-Mesh STA through a NAT so it appears to be one with the STA. The STA and this hidden network are represented by one MAC address. But this is not really a general link or solution because:
    It only works for Internet Protocol traffic.
    It restricts topologies.

## Slide 6: Method 1: 802.11 Mesh Can Act as an 802 LAN Segment
1
11
5
9
7
6
2
4
3
13
14
12
802 LAN
802 LANs
802.11
Mesh
MBSS
This problem is already solved for an 802.11 Mesh MBSS with Mesh Gates.
Mesh STA with
Mesh Gate
Mesh STA with
Mesh Gate
10
Mesh STA with
Mesh Gate
16
15
B
B

## Slide 7: Method 2: Currently You Can’t Use an Infrastructure Association as General Link
1
14
802 LAN
Associated STA
2
802 LAN
Associated STA
ESS
15
1
11
13
12
802 LAN
802 LAN
Infrastructure Association
Associated STA
AP With Portal
14

## Slide 8: Method 2: Currently You Can’t Use an IBSS Association as General Link
1
11
13
14
12
802 LAN
802 LAN
IBSS Association
STA
STA

## Slide 9: Method 3: NAT to One MAC
Multiple IP Hosts can hid behind a STA/NAT and all appear as one MAC address. For example:
1
11
13
12
802 LAN with IP Hosts
802 LAN
Infrastructure Association
Associated STA
AP With Portal
NAT
H1
H2

## Slide 10: Method 3: Problems
Standard NAT only works for IP protocol suite.
  Many of the protocols of concern to 802.1 AVB are non-IP.
Only supports a stub configuration where end stations are connected via an 802.11 connection.
  Method 2 does not provide a through link. Would not work with
1
2
3
4
5
802.3
802.3
802.3
802.11
802.3

## Slide 11: The Reflection Problem
In most cases, use of three or four-address data frames carries enough information; however, if a multicast frame originates from behind an infrastructure STA and is broadcast by the AP, the STA that sent it to the AP needs to know to ignore it.
Origin1
STA
AP
X
STA
STA

## Slide 12: The Reflection Problem
Solutions that don’t work so well:
  STA keeps track of the MACs “behind” it.
    Has scaling problems and mobility problems. What if Origin moves so as to be attached to X?
  Remember what frames you sent.
    Has scaling problems and mobility problems. What if Origin moves so as to be attached to X?
Origin1
STA
AP
X
STA
STA

## Slide 13: The Reflection Problem
My solution: for a multicast frame being sent by a STA to an AP from an origin behind the STA, use the already defined five address frame and include the infrastructure ingress STA address as such. Thus, when the STA gets the reflected frame from the AP, it knows that it sent it and can discard it.
Origin1
STA
AP
X
STA
STA

## Slide 14: 802.11 Extensions for Method 2
The technical details would be decided by a Task Group if one is created. But it is possible that the suggested facility would include adding the following optional capabilities to 802.11:
  Ability for a non-AP, non-Mesh STA to indicate that it supports this facility and has a portal.
  Ability to use
    the four-address format on IBSS hops and for infrastructure that is either a unicast or multicast AP / AP-portal originated frame, and
    the five-address format on multicast infrastructure STA / STA-portal originated frames.
  Ability for an AP to advertise that it supports this facility.

## Slide 15: Loop Prevention
Except inside an 802.11 mesh, where loop prevention is already solved, this is not 802.11’s problem.
The external network(s) should include mechanisms to stop loops.
  For example, 802.1 bridges using 802.1 loop prevention mechanisms.

## Slide 16: Loop Prevention
One possible solution is to recommend adding a bridge on the non-802.11-network side of each portal. This keeps general bridging outside of 802.11.
A Bridge is not always necessary, for example if an IP router is connected to the portal.
1
14
802 LAN
Associated STA
2
802 LAN
Associated STA
15
11
AP
B
B

## Slide 17: Motion to Form a Study Group
Motion:
Request approval by IEEE 802 LMSC to form an 802.11 Study Group on General 802.11 Links as described in doc 11-12/0589r2 with the intent of creating a PAR and five criteria.
  802.11 WNG TG vote:
  Moved: <name>, Seconded: <name>, Result: y-n-a
Moved by <name> on behalf of the WNG Standing Committee
  802.11 WG vote:
  Moved: <name>, Seconded: <name>, Result: y-n-a

## Slide 18: References
IEEE Std 802.11-2012, “… Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications”, 6 February 2012.