## Slide 1: Alternative Mesh Path Selection
Date: 2012-05-12
Authors:

## Slide 2: Abstract
802.11 Mesh provides the hooks to support a variety of path selection protocols and link cost metrics. Different network environments and applications may be best supported by different path selection protocols or link metrics. TRILL, as a proactive link state based path selection protocol, could be the basis for a useful alternative path selection protocol to HWMP.

## Slide 3: Contents
Background
TRILL
Liaison

## Slide 4: 802.11 Mesh Path Selection
802.11 Mesh, as was specified by its PAR, is designed to support multiple Path Selection protocols and multiple Link Metrics.
  All Mesh STAs in an MBSS (Mesh BSS) must use the same Path Selection protocol and Link Metric.
  The default Path Selection protocol and the only one specified in the 802.11 Standard is HWMP (Hybrid Wireless Mesh Protocol).
  The default Link Metric and the only one now specified in the 802.11 Standard is the Airtime link metric.
  Typically mesh paths are multi-hop. After each hop the receiving Mesh STA uses path selection to determine the next hop, if further forwarding is required. Path selection uses the link metric to decide what path is best.

## Slide 5: 802.11 Mesh Path Selection

## Slide 6: HWMP Path Selection Protocol
Hybrid Wireless Mesh Protocol: “Hybrid” because it uses two techniques:
  Proactively building spanning trees rooted at portals or other configured roots.
  Reactively finding paths to a specific destination when initiated by a source Mesh STA by processing flooded request frames and the reply from the destination. This part of HWMP is based on AODV (Ad-hoc On Demand Distance Vector).
Both of the above are Distance Vector techniques (see later slides).

## Slide 7: Airtime Link Metric
The Airtime Link Metric is based on the estimated amount of channel resources used to transmit a 8192 bit frame over the specific link.
  O = frame overhead, depend on PHY
  Bt = 8192 bits
  r = data rate in Mb/s
  ef = frame error rate for a 8192 bit frame

## Slide 8: Types of Path Selection
There are 2 types of path selection protocols.
      These are very general, basic descriptions!
Distance Vector
  Each node locally announces that it is a zero cost route to itself.
  Each node trusts what its neighbors say about their cost to various destinations, picks the best for each destination, adds the cost to that neighbor, and believes the sum is its cost to that destination through that neighbor.
Link State
  Each node finds its neighbors and the one hop cost to each neighbor. This data is reliably flooded to all nodes in the network.
  From this network wide neighbor data, each node can calculate the global topology and things like the optimum next hop.

## Slide 9: Types of Path Selection
Pros and Cons:
      These are very general characterizations!
Distance Vector
  Path selection is based on local view.
  Lower storage and computation cost at each node.
  Local cost calculation must be done before propagating changes.
Link State
  Path selection is based on a global view of the network permitting more intelligent decision making.
  Requires more storage and process at each node.
  Topology information update can be propagated after trivial check that is has not been previously received.

## Slide 10: Types of Path Selection
Pros and Cons:
      These are very general characterizations!
Reactive: Paths determined when needed.
  Typically a start up delay for a pair of nodes to communicate.
  Less overhead if only a few pairs of nodes communicate.
Proactive: All paths determined and maintained.
  No delay for a pair of nodes to communicate
  Less overhead if many pairs of nodes communicate.
Different mesh environments and/or applications may be best served by different Path Selection / Link Metric protocols.

## Slide 11: Contents
Background
TRILL
Liaison

## Slide 12: TRILL
The IETF TRILL Protocol is built on the IS-IS link state protocol. Devices that implement TRILL are called TRILL Switches or RBridges (Routing Bridges).
  TRILL provides transparent routing. It delivers the same frame as sent.
Basically a simple idea similar in structure to 802.11 mesh:
  Encapsulate native frames in a transport header providing a hop count.
  Route the encapsulated frames using link state routing.
  Decapsulate native frames before delivery.

## Slide 13: History
The use of TRILL for 802.11s path selection was discussed early. For example, during the following presentation made in 2004: 11-04/1462r0 “Routing and RBridges”
Early versions of the 802.11s draft included a link state routing protocol: RA-OLSR (Radio Aware – Optimized Link State Routing).
  For a brief period, HWMP was mandatory and RA-OLSR was optional in the draft but the forces to simplify the draft won and RA-OLSR was deleted from the 802.11s draft.

## Slide 14: IETF TRILL WG
TRansparent Interconnection of Lots of Links
  Current TRILL WG Charter
    http://www.ietf.org/dyn/wg/charter/trill-charter.html
  Co-chaired by
    Erik Nordmark, Cisco Systems
    Donald E. Eastlake 3rd, Huawei Technologies
  See also
    http://www.postel.org/rbridge/

## Slide 15: Some TRILL Features
Provides least-cost paths that are pro-actively computed with zero configuration.
Unicast forwarding tables at transit RBridges scale with the number of RBridges, not the number of end stations. Only edge RBridges need to learn end station (MAC) addresses.
Supports multi-pathing.
Supports frame priorities and VLANs.
Has a poem (see next slide)

## Slide 16: Algorhyme V2
I hope that we shall one day see
A graph more lovely than a tree.
A graph to boost efficiency
While still configuration-free.
A network where RBridges can
Route packets to their target LAN.
The paths they find, to our elation,
Are least cost paths to destination!
With packet hop counts we now see,
The network need not be loop-free!
RBridges work transparently,
Without a common spanning tree.
- By Ray Perlner

## Slide 17: Peering and Layers
TRILL operates at layer 2 ½. TRILL switches will peer with each other, both becoming part of a unified TRILL campus, through bridges but not through routers.
Layer 3:
TRILL Layer:
Layer 2:
Routers (plus servers and other end stations)
TRILL Switches
Bridges

## Slide 18: Peering and Layers
Router /End Station
Router /End Station
Bridge
Peers
Non-Peers
Bridge
Bridge
Peers

## Slide 19: Peering and Layers
Peers
Peers
Peers
Router /End Station
Router /End Station
TRILL Switch
TRILL Switch
Bridge(s)
TRILL Switch
Bridge(s)
Non-Peers

## Slide 20: Peering Between/Thru Meshes
If 802.11 meshes using TRILL are connected by bridged LANs, those TRILL instances peer with each other and form a unified campus, picking least cost paths, for example from A to B and from C to D below.
C
D
MBSS
MBSS
MBSS
A
B
802.3 LAN
802.3 LAN
802.3 LAN
B1
B2

## Slide 21: TRILL Standardization Status
Base Protocol approved as a standard in 2010.
Some RFCs that have issued:
  6325, “RBridges: TRILL Base Protocol Specification”
  6326, “TRILL Use of IS-IS”
  6327, “RBridges: Adjacency”
  6361, “TRILL over PPP”
Base Protocol Code Points Allocated
  Ethertypes: TRILL = 0x22F3, L2-IS-IS = 0x22F4
  Multicast MACs: 01-80-C2-00-00-40 to 01-80-C2-00-00-4F
  NLPID: 0xC0
  IS-IS code points (see RFC 6326)

## Slide 22: TRILL Open Source Status
Oracle: TRILL for Solaris
  http://hub.opensolaris.org/bin/view/Project+rbridges/WebHome
TRILL Port to Linux (in process): National University of Sciences and Technology (NUST),
Dr. Ali Khayam
Islamabad, Pakistan
  http://www.wisnet.seecs.nust.edu.pk/people/~khayam/index.php

## Slide 23: Work to Support TRILL in 802.11 Mesh Networks
It is likely that the following work on TRILL would be needed:
  Optimization of link state flooding.
    Useful for any richly connected TRILL campus.
  Encoding of TRILL frames in 802.11 mesh.
    TRILL currently standardized over 802.3 and PPP. Drafts exist for TRILL over IP and MPLS.
  Optimization of multi-destination data distribution.
  Mapping of Airtime Link Metric values to TRILL link metric.
    This is a simple numeric mapping. Perhaps ( ca * 25 * 104 ).

## Slide 24: Work in IETF or 802.11?
IETF TRILL WG
  Has TRILL expertise
  More work for TRILL
  Would provide a worked example of building on an 802 protocol using external interfaces in support of the 802 JTC1 SC.
IEEE 802.11 WG
  Has 802.11 expertise
  More work for 802.11

## Slide 25: Contents
Background
TRILL
Liaison

## Slide 26: Liaison Text
The IEEE 802.11 Working Group has no objection to the IETF TRILL Working Group standardizing a variation of the TRILL protocol for 802.11 mesh path selection. Such an alternative path selection protocol should use only external interfaces of the 802.11 mesh standard.
The 802.11 mesh standard is designed to support a variety of path selection protocols and link cost metrics, although only one of each can be in use at one time in a particular 802.11 mesh, so such an alternative path selection protocol would not be exclusive. Different path selection protocols and link cost metrics may be appropriate for 802.11 mesh under different circumstances.
If 802.11 code point allocation is required to support a TRILL based path selection protocol in 802.11mesh, 802.11 does have a mechanism by which such code points could be allocated to the TRILL WG, but approval of such allocations is not assured.

## Slide 27: Draft Liaison Envelope
To: Donald E. Eastlake 3rd and Erik Nordmark, IETF TRILL WG Co-Chairs
CC: Dorothy Stanley, IEEE 802.11 Liaison to the IETF
Ralph Droms and Brian Haberman, IETF Internet Area Co-Directors
Dan Romascanu, IETF Liaison to IEEE SA
<Body of Liaison from next slide>
Signed: Bruce Kramer, Chair 802.11 WG

## Slide 28: Liaison Motion
Motion:
Request the IEEE 802.11 WG chair transmit the liaison on slide 26 of “11-12-0621-02-0000-alternative-path-selection-protocol.pptx” to the IETF TRILL WG and any persons he deems appropriate.
Moved: <name>, Seconded: <name>
Result: y-n-a]

## Slide 29: References
IEEE Std 802.11-2012, “… Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications”, 6 February 2012.
IETF RFC 3561, “Ad hoc On-Demand Distance Vector (AODV) Routing”, July 2003.
IETF RFC 6325 (TRILL), “RBridges: Base Protocol Specification”, July 2011.