## Slide 1: Alternative Mesh Path Selection
Date: 2012-11-16
Authors:

## Slide 2: Abstract
The 802.11 Mesh standard provides the hooks to support a variety of path selection protocols and link cost metrics. Different network environments and applications are best supported by different path selection protocols and link metrics. There is interest in the IETF TRILL WG in specifying an alternative path selection protocol for mesh.

## Slide 3: Contents
Why
Background
TRILL

## Slide 4: Why Should 802.11 Be Interested?
802.11 mesh depends on a Path Selection and Link Metric protocol to determine how to forward frames. Different Path Selection protocols are best for different types of meshes.
Meshes differ along various dimensions and questions, such as:
  Fraction of pairwise multi-hop paths that will actually be in use.
  Density, dimensionality, and dynamism of mesh station location.
  Computational and storage capabilities of mesh stations.
  Can mesh path selection be local to an 802.11 mesh or should it be possible to optimize path selection on a wider scale possibly including multiple meshes and intervening nets?
  Should mesh stations have a global view of the mesh topology?

## Slide 5: Why Should 802.11 Be Interested?
There is only one path selection protocol specified in the 802.11 mesh standard. But it was realized, when 802.11s was developed, that different path selection protocols would be suitable for different mesh conditions.
Thus, 802.11 mesh is designed so that other path selection protocols can be deployed and agreed to by mesh stations.
There are successful 802.11 mesh products, but they use propriety path selection protocols.

## Slide 6: Why IETF TRILL?
The IETF TRILL protocol would provide a new type of 802.11 mesh path selection extending the utility of 802.11 mesh.
  – In particular TRILL is a proactive link-state path selection protocol designed from the beginning to support multi-access links.
Donald Eastlake, Co-Chair of the IETF TRILL Working Group was formerly Chair of the 802.11 Mesh Networking Task Group.
The TRILL WG has expressed interest in use of TRILL for path selection in IEEE 802.11s.
  – IETF Chair Liaison to IEEE 802.1, 10 May 2012
It would provide a worked example of building on an 802 protocol using external interfaces in support of the 802 JTC1 SC’s efforts.

## Slide 7: Contents
Why
Background
TRILL

## Slide 8: 802.11 Mesh Path Selection

## Slide 9: 802.11 Mesh Path Selection
802.11 Mesh is designed to support multiple path selection protocols and multiple link metrics because different mesh environments and applications can benefit from different path selection protocols and link metrics.
  All Mesh STAs in an MBSS (Mesh BSS) must use the same path selection protocol and link metric.
  The default path selection protocol and the only one specified in the 802.11 Standard is HWMP (Hybrid Wireless Mesh Protocol).
  The default link metric and the only one now specified in the 802.11 Standard is the Airtime link metric which estimates the amount of airtime to transmit an 8192 data bit frame.

## Slide 10: HWMP Path Selection Protocol
Hybrid Wireless Mesh Protocol: “Hybrid” because it uses two techniques:
  Proactively building spanning trees rooted at portals or other configured roots.
  Reactively finding paths to a specific destination when initiated by a source Mesh STA by processing flooded request frames and the reply from the destination. This part of HWMP is based on AODV (Ad-hoc On Demand Distance Vector).
Both of the above are Distance Vector techniques (see later slides).

## Slide 11: Types of Path Selection
Pros and Cons:
      These are very general characterizations!
Distance Vector
  Path selection is based on local view.
  Lower storage and computation cost at each node.
  Local cost calculation must be done before propagating changes.
Link State
  Path selection is based on a global view of the network permitting more intelligent decision making.
  Requires more storage and process at each node.
  Topology information update can be propagated after trivial check that is has not been previously received.

## Slide 12: Types of Path Selection
Pros and Cons:
      These are very general characterizations!
Reactive: Paths determined when needed.
  Typically a start up delay for a pair of nodes to communicate.
  Less overhead if only a few pairs of nodes communicate.
Proactive: All paths determined and maintained.
  No delay for a pair of nodes to communicate
  Less overhead if many pairs of nodes communicate.
Different mesh environments and/or applications are best served by different path selection protocols.

## Slide 13: Contents
Why
Background
TRILL

## Slide 14: IETF TRILL WG
TRILL is a Proactive Link State Protocol
TRILL supports multi-access links – and wireless links are inherently multi-access.

## Slide 15: More on TRILL
The IETF TRILL Protocol is built on the IS-IS link state protocol. Devices that implement TRILL are called TRILL Switches or RBridges (Routing Bridges).
  TRILL provides transparent routing. It delivers the same frame as sent.
At least one 802.11 mesh protocol stack implementing company is enthusiastic about implementing a TRILL based path selection protocol.

## Slide 16: Additional TRILL Features
Pro-actively provides least-cost paths with zero configuration. Supports multi-pathing.
Unicast forwarding tables at transit RBridges scale with the number of RBridges, not the number of end stations. Only edge RBridges need to learn end station (MAC) addresses.
Supports frame priorities and VLANs.
Has a poem (see last backup slide below)

## Slide 17: Peering Between/Thru Meshes
If 802.11 meshes using TRILL are connected by bridged LANs, those TRILL instances can peer with each other and form a unified campus, picking least cost paths, for example from A to B and from C to D below.
C
D
MBSS
MBSS
MBSS
A
B
802.3 LAN
802.3 LAN
802.3 LAN
B1
B2

## Slide 18: TRILL for Mesh Use Cases
Cases involving communication between many different pairs of mesh stations in a mesh, such as between between people in an independent group or between top-of-rack switches.
Cases where a global least cost path is needed involving more than one mesh or optimization over both mesh path choices and wired TRILL campus path choices.
Cases where a global knowledge of the mesh topology is useful to mesh stations.

## Slide 19: References
IEEE 802.11 TGs Usage Models, 11-04-0662-16-000s-usage-models-tgs.doc
IEEE Std 802.11-2012, “… Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications”, 6 February 2012
IETF RFC 3561, “Ad hoc On-Demand Distance Vector (AODV) Routing”, July 2003, http://www.ietf.org/rfc/rfc3561.txt
IETF RFC 6325 (TRILL), “RBridges: Base Protocol Specification”, July 2011, http://www.ietf.org/rfc/rfc6325.txt
IETF Liaison to IEEE 802.1, 10 May 2012, https://datatracker.ietf.org/liaison/1155/

## Slide 20: Back Up Slides

## Slide 21: Airtime Link Metric
The Airtime Link Metric in IEEE 802.11-2012 is based on the estimated amount of channel resources used to transmit a 8192 bit frame over the specific link.
  O = frame overhead, depend on PHY
  Bt = 8192 bits
  r = data rate in Mb/s
  ef = frame error rate for a 8192 bit frame

## Slide 22: 802.11 Mesh Use Cases
The use cases motivating the development of 802.11 mesh were as follows:
  Residential
  Office
  Campus/ Community/ Public Access Network
  Public Safety
  Military
IEEE 802.11 TGs Usage Models 11-04-0662-16-000s-usage-models-tgs.doc

## Slide 23: Types of Path Selection
Distance Vector versus Link State:
      These are very general, basic descriptions!
Distance Vector
  Each node locally announces that it is a zero cost route to itself.
  Each node trusts what its neighbors say about their cost to various destinations, picks the best for each destination, adds the cost to that neighbor, and believes the sum is its cost to that destination through that neighbor.
Link State
  Each node finds its neighbors and the one hop cost to each neighbor. This data is reliably flooded to all nodes in the network.
  From this network wide neighbor data, each node can calculate the global topology and things like the optimum next hop.

## Slide 24: TRILL Standardization Status
Some standards track RFCs that have issued:
  6325, “RBridges: TRILL Base Protocol Specification”
  6326, “TRILL Use of IS-IS”
  6327, “RBridges: Adjacency”
  6361, “TRILL over PPP”
  6439, “RBridges: Appointed Forwarders”
Base Protocol Code Points Allocated
  Ethertypes: TRILL = 0x22F3, L2-IS-IS = 0x22F4
  Multicast MACs: 01-80-C2-00-00-40 to 01-80-C2-00-00-4F
  NLPID: 0xC0; IS-IS code points (see RFC 6326)
TRILL has an open source software implementation for Solaris and one in progress for Linux.

## Slide 25: Peering and Layers
TRILL operates at layer 2 ½. TRILL switches will peer with each other, both becoming part of a unified TRILL campus, through bridges but not through routers.
Layer 3:
TRILL Layer:
Layer 2:
Routers (plus servers and other end stations)
TRILL Switches
Bridges

## Slide 26: Peering and Layers
Router /End Station
Router /End Station
Bridge
Peers
Non-Peers
Bridge
Bridge
Peers

## Slide 27: Peering and Layers
Peers
Peers
Peers
Router /End Station
Router /End Station
TRILL Switch
TRILL Switch
Bridge(s)
TRILL Switch
Bridge(s)
Non-Peers

## Slide 28: TRILL Open Source Status
Oracle: TRILL for Solaris
  http://hub.opensolaris.org/bin/view/Project+rbridges/WebHome
TRILL Port to Linux (in process): National University of Sciences and Technology (NUST),
Dr. Ali Khayam
Islamabad, Pakistan
  http://www.wisnet.seecs.nust.edu.pk/people/~khayam/index.php

## Slide 29: TRILL Work to Support 802.11 Mesh
It is likely that the following work on TRILL would be needed:
  Optimization of link state flooding.
    Useful for any richly connected TRILL campus.
  Encoding of TRILL frames in 802.11 mesh.
    TRILL currently standardized over 802.3 and PPP. Drafts exist for TRILL over IPv4/IPv6 and MPLS.
  Optimization of multi-destination data distribution.
  Mapping of Airtime Link Metric values to TRILL link metric.
    This is a simple numeric mapping. Perhaps ( ca * 25 * 104 ).

## Slide 30: Algorhyme V2
I hope that we shall one day see
A graph more lovely than a tree.
A graph to boost efficiency
While still configuration-free.
A network where RBridges can
Route packets to their target LAN.
The paths they find, to our elation,
Are least cost paths to destination!
With packet hop counts we now see,
The network need not be loop-free!
RBridges work transparently,
Without a common spanning tree.
- By Ray Perlner