## Slide 1: Block ACK Transmission
Date: 2012-05-14
Authors:

## Slide 2: Abstract
This presentation addresses a Block ACK transmission issue in IEEE 802.11ah, where asymmetric transmissions will likely to prevail

## Slide 3: Asymmetric Transmission
Ref: 802.11-12/0400r0 [ACK transmission]
AP to STN (Downlink) vs STN to AP (Uplink)
STN has more constraints as opposed to AP
  Transmission power (power amplifier etc)
  Capability
    Transmission capability (1 MHz vs AP with 2 MHz and beyond)
    Functionalities (AP may serve different types STN)
Use Cases
  Use Case 3 : Extended range Wi-Fi
  Use Case 1: Sensors and meters

## Slide 4: Problems for Normal ACK
Ref: 802.11-12/0400r0 [ACK transmission]
  STN can receive data but AP may not receive ACK
  Simple Fix: allow STN to use lower MCS or narrower bandwidth for ACK
Ref: 802.11-12/0324r1 [Short ACK]
  Short ACK helps with lowest MCS in SIG but not with narrower bandwidth
  May result in downlink using narrower bandwidth unnecessarily

## Slide 5: Problem for Block ACK
Block ACK
  Improves channel efficiency by aggregating several ACKs
Problem in asymmetric cases: (b) Data & Block ACK phase
  Multiple downlink data MPDUs use lower MCS or narrower bandwidth than necessary
  Not efficient use of channel
  BlockAck payload can be large
    ~ 214 bytes
  Short ACK may not applicable
Use Cases
  Use Case 3 : Extended range Wi-Fi
  Use Case 1: Sensors and meters

## Slide 6: Proposal
Basic idea
  Determine uplink and downlink MCS and bandwidth in BlockACK setup phase (Management frame ADDBA)
  May use Short ACK to help
Block ACK setup steps (ADDBA)
ADDBA Request
  STN records successful Downlink MCS and BW from AP
ADDBA Response
  STN informs AP the preferred MCS and BW for downlink

## Slide 7: Comparison
Current
Proposed
(Short)
(mod)

## Slide 8: Implementation Example
ADDBA Request: STN records successful Downlink MCS and BW
ADDBA Request
ADDBA Request
X
ADDBA Request
ShortACK
Try
Try lower MCS, same BW
( config “A”)
Try lower MCS, narrower BW
(config “B”)
ShortACK
X
X
ADDBA Response
STN may send ADDBA Response
AP
STN
STN notes “config A”

## Slide 9: Implementation Example (cont’d)
ADDBA Response: STN informs AP the preferred MCS and BW for downlink (config “A”)
  Could be part of Status Code or a new field
ADDBA Response
ADDBA Response
X
X
ADDBA Response
ShortACK
AP
STN
Try same MCS & BW as config “B”
Try lower MCS, same BW
(config “C”)
Try lower MCS, narrower BW
(config “D”)
AP notes “config A”
for downlink and
“config D” for uplink
STN notes “config D” for uplink

## Slide 10: Block Transmissions and ACK
AP uses config “A”
STN uses config “D”
AP
STN
NAV to include
config “A” + “D”
Data and Block ACK transmission

## Slide 11: Conclusions
In 11ah, Block ACK from STN may not reach AP
  AP may transmit at higher power and better off in capability
  STN can receive Data but its ShortACK or BlockACK may not reach AP
  Downlink may have to use lower MCS or BW than necessary
Propose to allow Block ACK Response to include preferred MCS and BW information

## Slide 12: Straw Poll 1
Do you agree to allow STN transmit Block ACK with lower (or more robust) modulation and coding rates than that of received frames from AP?

## Slide 13: Straw Poll 2
Do you agree to allow STN transmitting Block ACK with narrower bandwidth PHY after received frames from AP?

## Slide 14: Straw Poll 3
Do you agree to use the following procedure for Block ACK transmission
(Short)
(mod)