## Slide 1: LB187 Proposed Resolution to CID 5274
Date: 2012-05-08
Authors:

## Slide 2: CID 5274
For VHT wider channel width operation, when a CF-End is sent by a TXOP holding VHT STA or VHT AP to truncate the TXOP on primary and secondary channels, it will reset the NAV for STAs associated with the same VHT BSS but not for neighboring BSS VHT STAs on the secondary channels that had their NAV set by the TXOP holder. So the neighboring BSS VHT STAs for which the primary channel is the TXOP holder's secondary channel are at a disadvantage and will be unfairly denied channel access. Given that there will be dense deployment of VHT devices such scenarios are very likely to occur and lead to poor performance. This unfairness issue for VHT STAs needs to be resolved.

## Slide 3: Proposed Change for CID 5274
Update TXOP truncation rules with CF-End for VHT AP and VHT STAs to remove this unfairness in channel access for VHT STAs.

## Slide 4: Proposed Resolution for CID 5274
  Insert following text in 9.19.2.7 : A VHT STA that uses a non-HT duplicate frame to establish protection of its TXOP shall send any CF-End frame in non-HT duplicate format on primary and all secondary channels on which it transmitted during its TXOP.
    Clears NAV at STAs that can hear TXOP holder on primary and all secondary channels
  Change following text in 9.19.2.7: After receiving a CF-End with a matching BSSID(TA) without comparing Individual/Group bit, an AP may respond by transmitting a CF-End frame after SIFS on the primary channel and all secondary channels on which CF-End was received.
    Clears NAV at STAs that can hear TXOP Responder on primary channel of the same BSS
  Insert following text in 9.19.2.7: After receiving a CF-End with a non-matching BSSID(TA) without comparing Individual/Group bit, an AP may respond by transmitting a CF-End frame after SIFS on its primary channel.
    Clears NAV at STAs, set by a non-BSS device

## Slide 5: Summary
Proposed resolution for CID 5274
  Proposed text changes to Section 9.19.2.7 Truncation of a TXOP

## Slide 6: Questions / Comments ?
Thank You!

## Slide 7: References
802.11-2012
802.11ac D2.0

## Slide 8: Straw poll 1
Do you agree with the resolution described in Slide 4
  Yes
  No
  Abstain