## Slide 1: BF Corrections presentation
Date: 2012-06-14
Authors:

## Slide 2: Scope
The purpose of this presentation is to list and explain the proposed corrections to the BF and the link adaptation that are proposed.
Most of changes are dealing with performing of BF in allocated CBAP.
Other changes are corrections/simplifications

## Slide 3: Proposed Changes
Grant/Grant ACK
Don’t allow sector sweep to break across allocations
Enabling Multi-Antenna BF in CBAP
Enabling Multi-Antenna BF in short allocations
Allowing double RXSS
Making RXSS in A-BFT optional
Defining the accuracy of 6xSIFS and 3xSIFS intervals
Allowing A-BFT to contain one slot.
Link Measurement
BRP aggregation
MIDC corrections

## Slide 4: Grant/ Grant ACK
Use when trying to initiate SLS before the link is lost in CBAP
RTS/CTS are used to make sure the link was not lost yet.
If first sequence is used, not sure the destination received the grant .
Grant /Grant ACQ enables dynamic control of the multi-antenna BF parameters – total number of sectors and number of receive antennas
Grant enables synchronization (of the start of the BF training between the initiator and responder) – necessary for efficient multi-antenna BF.
RTS
CTS
Grant
SSW
SSW
Grant
Grant/ACK
SSW
SSW
SSW

## Slide 5: Proposed Solution
Define a new packet type Grant ACK
Allow the use of Grant/Grant ACK combination only to request SLS in CBAP.
Protocol
  if inside a TXOP, send a CF_end, then PIFS and then the grant Grant ACK
  Outside TXOP, send the grant.
  Starting an SLS with Sector Sweep packet still works.

## Slide 6: Do not allow SSW to break across allocations
Reason: Due to guard time, the initiator and responder are not synchronized in the beginning of the allocations, (up to 16usec). Therefore the first packet in sweep may be lost.
another issue is how to start an RSS when the next allocation owner is the ISS initiator.
TXSS
TXSS
TXSS
TXSS
Start of allocation in initiator
Start of allocation in Responder
Guard Time = 16usec

## Slide 7: Multi-Antenna BF in CBAP
Enable Grant/Grant ACK to control the number of elements/antennas to be used in the sweep to enable working in short allocations.
Allow DMG antenna switching in CBAP for SLS
Enable Multi-Antenna BF after link loss.
  slightly different behavior
  Text is not mandatory

## Slide 8: Allowing Double RXSS
Proposed Solution (bottom graph)
Small text change in description on BF control field.
TXSS
TXSS
FBCK
ACK
Grant
TXSS
RXSS
FBCK
ACK
Grant
RXSS
TXSS
FBCK
ACK
Current RXSS for BF training between two antenna arrays (above)
TXSS
RXSS
FBCK
ACK
Grant
RXSS
RXSS
FBCK
ACK

## Slide 9: Making RXSS in A-BFT optional
Currently it is mandatory for a PCP to have RXSS in A-BFT every dot11ABFTRRXSSSwitch.
We prefer to remove this requirement as it complicates the implementation of A-BFT.
Due to the fragmented nature of BTIs, it does not really help a device which prefers to associate using RXSS.
Connection range is not compromised

## Slide 10: Defining the accuracy of 6xSIFS and 3xSIFS intervals
The accuracy of these intervals is undefined.
We prefer to set it to 10% of aSlotTime  0.5usec
10% of the interval may introduce an inaccuracy which it too large.
Two new IFS intervals defined:
  MBIFS for 3xSIFS
  LBIFS for 6xSIFS

## Slide 11: Allowing A-BFT to contain one slot
Currently it is mandatory to have at lease two slots.
This complicates the A-BFT
We prefer to remove this requirement.
Although this is a useful feature, it does not need to be mandatory on every A-BFT, and can be operated dynamically in situations where BF with several devices is expected.

## Slide 12: Link Measurements
Add a capability bit that define that a response to a link measurement request will be arrive in a defined time.
Allow a default value for the link margin.
  make it optional
Define the PER requirement for the MCS feedback.
  make it 10-2
Define the PER requirements in TSPEC to be 10-1, 10-2, 10-3 rather than 10-3, 10-4, 10-5
Add a request for BF to the activity fields

## Slide 13: BRP aggregation
Current text is unclear.
Allow aggregation of BRP frame with other frames in an A-MPDU only when the other frames are either ACK or BACK or QoS-Null Data.
Aggregation of more than one BRP frame is not allowed.

## Slide 14: Update to MIDC
Clarification of the BRP setup protocol in the case the MID only is requested
Defining MID+BC to be a single protocol (if both are requested, both need to granted)
Removing contradiction between 9.35.3.2 and 9.34.6.3.6.3

## Slide 15: Backup