## Slide 1: Efficient Probe Filtering
Date: 2012-07-05
Authors:

## Slide 2: Abstract
Several submissions to TGai have proposed probe filtering schemes, such as inclusion/exclusion lists and regular expressions, in order to reduce the number of unnecessary probe responses generated by probe requests. This proposal suggests an alternate filtering mechanism that is more efficient for an AP STA to evaluate than other proposed schemes.
This proposal is submitted as an alternative approach to consider should the task group choose to include probe filtering in the TGai amendment.

## Slide 3: Concept
The concept presented in this submission is to use bit masking to enable complex inclusion filters to be implemented in such a way that the filter is trivial for an AP to evaluate when processing a probe request. The filtering mechanism implements a Boolean expression of the form:
Respond = (SSID_1 || SSID_2) && (HESSID_A || HESSID_B) || …
The filter expression is computed by the probing STA and transmitted as a Filter Element in a probe request. Each receiving APs uses the Filter Element and a pre-computed mask, based on its configuration, to avoid responding to a probing STA that is uninterested.
The filter is not perfect, but thins the number of responses by eliminating a potentially large percentage of undesired probe responses.

## Slide 4: Filter Element-based Active Scanning
STA
AP2
AP1
Probe Request (Filter Element,…)
Probe Response
Filter Element & Mask2 == Mask2
&&
Pre-FILS Conditions Match
(Respond)
Filter Element & Mask1 != Mask1
(Do not respond)
Filter Element – bit mask computed by STA from fixed list of filtering parameters (e.g. SSID, HESSID, etc)
Maskn – bit mask that is pre-computed by APn. The mask is pre-computed using the same algorithm used to compute the Filter Element
The filter check on AP is a simple mask and compare operation, making it lightweight computationally
The filter test will not eliminate all unnecessary probe responses, but it could eliminate a large percentage of them in many cases
Doing filter test prior to pre-existing tests provides an efficient pre-filtering mechanism
Absence of Filter Element in probe request results in current behavior

## Slide 5: Filter Element
F1
F2
F3
F4
F5
Fn
Filter Element is a bitmask consisting of a number of sub-filters (F1 - Fn)
Each sub-filter consists of a portion of the bitmask related to a particular filtering parameter, such as SSID or HESSID. The list of filtering parameters is TBD.
Values of interest are hashed to select a single bit in the mask (note: multiple values of a single parameter will hash to each bit but a particular value will map to only one bit)

## Slide 6: Filter Element Construction
For each value of interest, compute its single-bit bitmask:
Fx = 0x1 << ((hash(param_x) % N_BITS_Fx) + Fx_SHIFT)
Bitwise OR all of the bitmasks together to construct the Filter Element
Lists of parameter values are handled by computing the above mask for each list element and including it in the above bitwise OR
ANY (wildcard) is specified by setting all bits in a particular sub-filter
Concatenation of all sub-filters into the filter implicitly results in a Boolean AND of all of the sub-filters

## Slide 7: AP Mask Construction
For each sub-filter element, compute its single-bit bitmask based on the AP’s value for the associated parameter:
Fx = 0x1 << ((hash(param_x) % N_BITS_Fx) + Fx_SHIFT)
Bitwise OR all of these sub-filter bitmasks together to construct the AP’s Mask
Note: This is pre-computed based on AP configuration rather than being computed for each probe request

## Slide 8: Filter Evaluation
AP evaluates filter while processing each probe request:
if (Filter Element present) {
if ((Filter Element & AP Mask) != AP Mask) {
// do not respond
}
}
/ / continue with normal probe request handling

## Slide 9: Conceptual Example
 | Probe Filter | BSS 1 | BSS 2 | BSS 3
AP Mask |  | 0x01020408 | 0x02102040 | 0x04800408
STA 1 | 0x02ffffff | Omit | Respond | Omit
STA 2 | 0xff80ffff | Omit | Omit | Respond
STA 3 | 0xff020408 | Respond | Omit | Omit
TG defines filter with 4 8-bit sub-filters
  F1 assigned to SSID, F2-F4 assigned to other parameters, #2 through #4
Enterprise AP beaconing 3 SSIDs, BSS 1 and BSS 3 have the same parameter values for filter parameters #3 and #4
STA 1 probing for BSS 2 SSID
STA 2 probing for BSS 3 SSID
STA 3 probing for any SSID with a combination of parameter 2 through 4 desired values. Only parameter #2 values differ between BSS 1 and BSS 3
F1
F2
F3
F4

## Slide 10: Motion
Move to add the following text to Clause 6.1.6 Omission of Probe Response of the TGai Specification Framework Document (11-12/0151r09): “A FILS capable STA may include a probe response filtering bitmask element in a probe request as outlined in 11-12-0775r0. A FILS capable AP STA receiving a probe request with a probe response filtering bitmask element should apply the filter, as outlined in 11-12-0775r0, to omit issuing a probe response if the filter indicates a response is not required.” Moved: Seconded: Vote: Y/N/A