## Slide 1: Short Beamforming Report Poll Frame
Date: 2012-07-15
Authors:

## Slide 2
Authors:

## Slide 3
Authors:

## Slide 4: Abstract
Short ACK and short CTS have been introduced to 802.11ah spec framework, with similar format design.
we propose that the similar design principle could be extended to Beamforming Report Poll frame to further reduce overhead.

## Slide 5: Background
In current 11ah spec framework, the short Ack and fast RTS/CTS are designed with STF, LTF1, and one SIG field.
In the proposed short frame formats, the SIG field only contains information needed for those frames.

## Slide 6: Discussion
  Based on the similar logic as short ACK, the function of Beamforming Report Poll frame can also be compressed, when Beamforming Report Poll frame is transmitted using:
    2MHz bandwidth
    single stream, and
    fixed MCS.
  Therefore, we propose a short Beamforming Report Poll frame format with only STF, LTF1, and a special SIG field, same as short preamble for 2MHz.
  The indication of short Beamforming Report Poll frame could be included in SIG field , using the reserved MCS value, similar as Short ACK indication.
STF
LTF1
SIG

## Slide 7: Current SIG-A field for 2MHz as defined in 11ah Spec framework
 | SU(short) | MU(long)
Length / Duration | 9 | 9
MCS | 4 | 
BW | 2 | 2
Aggregation | 1 | 
STBC | 1 | 1
Coding | 2 | 5
SGI | 1 | 1
GID |  | 6
Nsts | 2 | 8
PAID | 9 | 
ACK Indication [11] | 2 | 2
Reserved | 5 | 4
CRC | 4 | 4
Tail | 6 | 6
Total | 48 | 48

## Slide 8: Short Beamforming Report Poll frame SIG Design
SIG Field | Bits | Comments
AP Address | 9 | Indicate Partial AID of the beamformer
MCS | 4 | MCS (a reserved MCS value indicates special SIG for Beamforming Report Poll,e.g.15 for short Ack frame,14 for Beamforming Report Poll and 12/13 for RTS/CTS)
STA Address | 13 | Indicate Partial AID of intended beamformee
End of TXOP | 2 | Set to 0 to indicate this frame exchange is not the end of TXOP
Segment retransmission bitmap | 8 | The conception of segment transmission in 11ah needs further study.
CRC | 4 | 4 bits of CRC should be enough
Tail | 6 | Same as normal 2MHz SIG
Reserved | 2 | 
Total | 48 | Only applies to 2MHz SIG

## Slide 9: Short Beamforming Report Poll frame SIG Design
In a short Beamforming Report Poll frame, the SIG field includes, for example,
  AP address (9 bits)
  MCS (4 bits, using the reserved MCS value to indicate the frame type)
  STA address (13 bits)
  TXOP end (2 bits). This field is set to 0, to indicate those receivers without matched AP or STA address shall not contend for transmission until it receives another frame exchange with TXOP_END equals to 1. This field can be further reduced.
  Segment retransmission bitmap( 8 bits). The max segment number could be further reduced to 4 since 11ah only needs to support max 4 antenna. (FFS)
  CRC (4 bits)
  Tail (6 bits)
  Reserved (2 bits)

## Slide 10: STA Address and AP Address Fields
When an AP sends a Beamforming Report Poll frame to an STA, the STA address field carried in the frame indicates the receiver address and the AP address field indicates the transmitter address.
When an STA sends a Beamforming Report Poll frame to an AP, the STA address field indicates the transmitter address and the AP address field indicates the receiver address.
9 bits AP address is enough to identify the involved AP/BSS and 13 bits STA address is enough to identify the STA in the BSS.
The positions of STA address and AP address are fixed in SIG.

## Slide 11: Pros vs. Cons
Pros:
  Reduced overhead
  Less confliction possibility.
Cons:
  Replaced transmitter/receiver address field with STA/AP address field.

## Slide 12: Conclusion
Based on the example SIG design, we feel it’s logic and feasible to define a Short Beamforming Report Poll frame format with only STF, LTF1, and a special SIG in current 802.11ah spec framework.

## Slide 13: Pre-motion
Do you agree to add in spec framework that 11ah shall define a short Beamforming Report Poll frame format using short preamble format as described in slide 6 (SIG field content TBD).
Y
N
A
Slide 13

## Slide 14: Motion
Motion to accept to add in spec framework that 11ah shall define a short Beamforming Report Poll frame format using short preamble format as described in slide 6 (SIG field content TBD).
  Y:
  N:
  A:
Slide 14