## Slide 1: Non-linear Multiuser MIMO for next generation WLAN
Date: 2012-07-13
Authors:

## Slide 2: Abstract
  This contribution provides an overview of non-linear MU-MIMO, focusing on the correlated LOS indoor MIMO channel.
  Simulation of linear vs. non-linear MU-MIMO
  Experimental results
Measurements were performed in an indoor LOS environment. Throughput performances of the non-linear MIMO system were superior to linear MIMO.

## Slide 3: Introduction
WLAN data traffic has been growing quite rapidly.
  An increasing number of WLAN equipped devices.
  Large data file or high-definition video is transmitted over WLAN.
  WLAN is used for data traffic offload from the cellular network.
Future WLAN/mobile communication systems will need to provide robust and high-capacity transmission to many users.
Multiuser MIMO (MU-MIMO) is one of the key technologies to improve both area throughput and user throughput.
  TGac include DL MU-MIMO as an optional mode.
  3GPP LTE and LTE-Advanced adopted MU-MIMO.
  Based on linear precoding.

## Slide 4: Usage Environment
Multiple users simultaneously use WLAN at conference room, lobby etc.
  High capacity needed.
  In an indoor Correlated LOS MIMO channel.
  Non-linear MU-MIMO will be needed.

## Slide 5: MU-MIMO in a small sized cell
Linear precoding/combining
  Low computational complexity.
  Weak point  Correlated channel condition
    Spatial channel correlation becomes rather high due to the increase of LOS probability.
Non-linear precoding/combining
  Higher achievable sum rate than linear MU-MIMO, especially over spatially-correlated MIMO channels.
  Increased computational complexity compared to linear MU-MIMO.
  Examples of non-linear algorithms:
    Iterative soft interference canceller (Turbo-SIC)
    Tomlinson-Harashima precoding (THP)
    Vector perturbation (VP)

## Slide 6: MMSE and Vector Perturbation
VP
MMSE
filter
modulo
MMSE filter
Obtain precoding gain by VP
MMSE
VP
～
～

## Slide 7: Vector Perturbation
Tx side
Rx side

## Slide 8: Simulation settings
Sampling rate | 30.72 Msamples/s
FFT size | 2048
Number of subcarriers | 1200
Number of antennas | 4 (BS), 2 (UE)
Number of users | 2
Direction of UEs from BS (deg.) | -2.38, 2.38
Modulation coding scheme | 16QAM (3/4) , 64QAM (3/4)
Channel coding | Turbo code
Decoding algorithm | SOVA (6 iterations)
Array configuration | Uniform linear array
Antenna spacing | 1.0 wavelength @ DL carrier frequency (BS)
 | 0.5 wavelength @ DL carrier frequency (UE)
Carrier frequency | 3.36 GHz (DL)
Spatial filtering | MMSE with perfect SNR estimation
Perturbation vector search | QRDM - E (S = 7, M = 7)
シミュレーション諸元
Layout

## Slide 9: WINNER II Channel model
Two scenarios have been selected for the simulation

## Slide 10: WINNER II A1 indoor office LOS
The spectrum efficiency of VP is double that of MMSE at around 24dB SNR and above.
  Spectrum efficiency of 16QAM is 12 b/s/Hz.
16QAM
64QAM
16QAM
64QAM

## Slide 11: WINNER II B3 large indoor hall LOS
The spectrum efficiency of VP is double that of MMSE at around 21dB SNR and above.
  Spectrum efficiency is 12 ～ 18 b/s/Hz
16QAM
64QAM
16QAM
64QAM

## Slide 12: Measurement setup
 | Parameter | BS | UE
Baseband | Precoding | Linear:MMSE Nonlinear:Vector Perturbation | None
 | Multiplex mode | OFDM-SDM (MU-MIMO) | OFDMA (SIMO)
 | Modulation scheme | QPSK, 16QAM, 64QAM | 
 | Number of subcarriers | 1200 | 
RF | Frequency | 3.36 GHz | 3.26GHz
 | Bandwidth | 20 MHz | 20MHz
 | TX power | 4 W Max. | 1 W Max.
Antenna | Type | Monopole antenna , 2.1dBi | 
 | Number of elements | 4 | 2
 | Element spacing | 1 l | 0.5 l
 | Height | 3.0m | 1.8m
In order to form a 4 × 4 MU-MIMO, 1 BS and 2 UE’s were used.

## Slide 13: MCS
This MCS based on LTE-Advanced system.

## Slide 14: Measurement Equipment
RF Unit
Baseband
Unit
Antenna
BS
UE

## Slide 15: Measurement Environment
18m
Large
Window
7.2m
Ceiling Height:12m
3.0m
1.8m

## Slide 16: Throughput
Throughput performance of the VP algorithm is superior to that of the MMSE.
  20 to 30% higher throughput
16QAM
64QAM
16QAM
64QAM
UE distance = 1.0m, Pout=3dBm Max.
UE distance = 1.5m, Pout=3dBm Max.
30%
20%

## Slide 17: Block Error Rate (BLER)
MCS19: 64QAM, R=0.73
MCS14: 16QAM, R=0.77
At the higher MCS, BLER of non-linear MIMO is lower than linear MIMO.

## Slide 18: Conclusions
In future WLAN is needed to extend system capacity.
Proposed non-linear MU-MIMO is one of the key solutions.
Performances of the non-linear MU-MIMO in indoor LOS environments were better than linear MU-MIMO in our measurements.
This work is supported by the Ministry of Internal Affairs and Communications under a grant entitled "Research and development on nonlinear multiuser MIMO technologies."

## Slide 19: Future Work
We will perform additional measurement campaigns in several environments and other MIMO configurations.
  Measurement in auditorium, corridor etc.
  8 × 8 MIMO configuration.