## Slide 1: Spectrum access and Tx control for regulatory conformance
Authors:
Date: Jul. 17, 2012
Name | Company | Address | Phone | email
Shusaku Shimada | Yokogawa Co. | 2-9-32 Nakacho Musashino-shi, Tokyo 180-8750 ,Japan | +81 42 252 5558 | shusaku@ieee.org
Stefan Aust | NEC Communication Systems, Ltd. | 1753 Shimonumabe, Nakahara-ku, Kawasaki, Kanagawa 211-8666, Japan | +81 44 435 1177 | aust.st@ncos.nec.co.jp
Mitsuru Iwaoka | Yokogawa Electric Co. | 2-9-32 Nakacho Musashino-shi, Tokyo 180-8750 Japan | +81 42 252 5558 | Mitsuru.Iwaoka@jp.yokogawa.com
Yusuke Asai | NTT | 921A, 1-1, Hikarinooka, Yokosuka, Kanagawa 2390847 | +81 46 859 3494 | asai.yusuke@lab.ntt.co.jp
Huai-Rong Shao | Samsung Electronics | 3000 Orchard Parkway, San Jose, CA 95134 | +1 408 544 2754 | hr.shao@samsung.com
Zander Lei | Institute for Infocomm Research | 1 Fusionopolis Way,#21-01 Connexis Singapore 138632 | +65 6408 2436 | leizd@I2R.A-STAR.EDU.SG

## Slide 2: Background
Each regional regulatory body typically implements similar and normative requirements in term of sub-1GHz band, including listening duration and detection threshold level of LBT (listen before talk) function, Tx control functions such as duty cycling, maximum Tx (on) time and Tx idle (off) period (gap).

## Slide 3: A provision to add in Specification framework
PHY and MAC management entity of 11ah shall provide appropriate parameters (TBD) of PLME and MLME service primitives to support Spectrum access and Tx Control functions in order to comply to each regulatory domain.
These appropriate parameters to be added are TBD so far, but are supposed to be a part of “behavior limit set” entry in the Annex Table which correspond to new operating classes of 11ah.
Slide 3

## Slide 4: An example (TBD)
The annex D and Annex E provide information and specifications for operation in many regulatory domains.
Annex D (normative) Regulatory references
    D.1 External regulatory references
    D.2 Radio Performance Specifications
      D.2.6 CCA-ED threshold of 11ah (TBD)
        For OFDM PHY operation with CCA-ED, the thresholds shall be less than or equal to –82 dBm for 2 MHz channel widths, –85 dBm for 1 MHz channel widths.
Annex E (normative) Country elements and operating classes
    E.2 Band-specific operating requirements
      E.2.3 915.9–928.1 MHz in Japan (TBD)
        STAs shall use the following:
          CCA-ED (D2.6 (CCA-ED threshold) is overridden by TBD value for LBT)
            For OFDM PHY operation in this specific band, the CCA-ED thresholds shall be less than or equal to -80dBm for 1 MHz channel widths.
          LDC up to 10% or 360s/1 hour
          Tx on/off time control is as 400ms max On time /2ms min OFF time

## Slide 5
Straw poll
Do you agree …
to include the proposed text on slide 3 into the specification framework document in order to comply to each regulatory domain?
  Yes
  No
  Abstain

## Slide 6: References
[1] Europe: ETSI EN 300 220-1 V2.3, 2009
[2] Japan: Doc.: 11-12/0534r0, “Summary of latest Japanese 920MHz rules
and conditions” 2012-05-15
[3] Korea: Doc.: 11-11/685r0, 11-11/1422r0, “S1G Spectrum Regulations Outside the US”
[4] Singapore : Doc.: 11-12/111r1, “Singapore Sub 1GHz Frequency Bands and Channelization for IEEE 802.11ah”
[5] New Zealand and Australia : TBD

## Slide 7
End
Slide 7